## Slide 1: CS 168 Designing a Network
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2: Administrivia
Discussion sections start Wed., Sep 9
Reading assignments up for this week
This week: basics, philosophy, principles,…
Next week: routing!
Very full lecture today (100 slides!)

## Slide 3: Today
What do today’s access networks look like?
  Just for context
How would you build the rest of a network?
  Keys are efficiency and reliability
Packet dynamics
  Delays, queues, and all that….

## Slide 4: Remember our Internet Diagram
end-system
switch
link

## Slide 5: ISP Technologies
ISPs have very similar backbone technologies to connect regions and connect to each other
But they differ substantially in their “last mile”
  The “access technology” that reaches the consumer

## Slide 6: Some ISPs are phone companies
phone company

## Slide 7: Telephony Access Technology
phone company

## Slide 8: Last Mile (logically)
home PC
switch

## Slide 9: Last Mile (in reality)
home PC
switch
DSL modem
DSLAM
central office
phone line
telephone
telephone network
...

## Slide 10: Digital Subscriber Line (DSL)
Twisted pair copper
3 separate channels
  Downstream data channel
  Upstream data channel
  2-way phone channel

## Slide 11: AT&T Central Offices in Bay Area

## Slide 12: AT&T Central Office in Berkeley

## Slide 13: Cable Access Technology
home PC
switch
cable modem
CMTS
cable head end
copper
fiber
...

## Slide 14: Many households share access
switch
CMTS
fiber
cable head end

## Slide 15: Cable
Coaxial copper & fiber
Shared broadcast medium
  Why?

## Slide 16: Enterprise Access Technology
workstation
“aggregate” switch
Ethernet cable
“local” switch
...

## Slide 17: Ethernet
Twisted pair copper
1 Gbps, 10 Gbps, 100Gbps (each direction)

## Slide 18: Other access technologies
Cellular (smart phones)
Satellite (remote areas)
Fiber to the Home (home)

## Slide 19: Access Technologies
From an architectural perspective…
  Access technologies are a boring detail
  Logical equivalent of a wire to the first-hop switch
From an infrastructure perspective…
  That’s where all the money goes
  Deployment, maintenance, speed limitations, etc.
We won’t discuss access networks any more
  But this is what keeps ISP CEOs up at night…
  Routing protocols, etc., are the least of their problems..

## Slide 20: What about the rest of the network?
Access technologies are specialized
What about the rest of the network?
How do you scale such a network?
  Billions of endpoints!

## Slide 21: What about this design?
Advantage:
  Every source-destination pair has its own link
Disadvantages:
  No sharing
  Would require too many links O(n2)

## Slide 22: What about this design?
Advantage:
  Lots of sharing
Disadvantages:
  Too much sharing
  Per-node capacity O(1/n)
  Not very resilient

## Slide 23: What about this design?
Advantage:
  Lots of sharing
Disadvantages:
  Too much sharing
  Per-node capacity O(1/n)
  Not very resilient
Last two designs were used for local area nets
  Bad for wide area networks

## Slide 24: Requirements for network topology
Resilient to failures
  Several paths between each source and destination
Enough sharing to be feasible
  Number of links not too high
Provide adequate per-node capacity
  Number of links not too small

## Slide 25: Switched Networks
Provide reasonable and flexible compromise

## Slide 26: Requires sharing of links/switches
shared link and switch resources

## Slide 27: Two approaches to sharing
Reservations:
  “Flows” reserve bandwidth needed in advance
  Must reserve their peak bandwidth
On demand: (also known as “best effort”)
  Send packets when you have them
  Hope for the best….

## Slide 28: Example of “Statistical Multiplexing”
Statistical multiplexing:
  Combining demands to share resources efficiently
  Long history in computer science
    Processes on an OS
    Cloud computing
    …
Reservation: sharing at flow level
On-demand: sharing at packet level

## Slide 29: Which is better?

## Slide 30: Example: three constant sources
Total bandwidth 30Mbps
Demands: Each source needs 10Mbps
Reservation and on-demand give same result
  Every source gets what they need
  No wasted bandwidth
  ….

## Slide 31: Example: Three “bursty” sources
12Mbps
Time
Link capacity = 30Mbps
11Mbps
13Mbps

## Slide 32: What happens with reservations?
12Mbps
Option #1: allow two flows to reserve peak rate
Time
Link capacity = 30Mbps
11Mbps
13Mbps
Must turn away third flow!

## Slide 33: What happens with reservations?
12Mbps
Option #2: allow flows to reserve equal rates
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading!

## Slide 34: What happens with on-demand?
No overloading
Time
Link capacity = 30Mbps

## Slide 35: Peak vs Average Rates
For each flow, define:
  P = peak rate
  A = average rate
Reservations must reserve P:
  But flows only use A (on average)
  Level of utilization is A/P
On-demand:
  Can achieve higher utilizations
  Depends on degree of sharing, burstiness of flows
  Peak of aggregate approaches sum of averages

## Slide 36: Smooth vs Bursty Applications
Some apps have relatively small P/A ratios
  Voice might have a ratio of 3:1 or so
Data applications tend to be rather bursty
  Ratios of 100 or greater are common
That’s why the phone network used reservations
  And the Internet does not….
  More in next lecture

## Slide 37: Two approaches to sharing
Reservations
On demand
How are these implemented?

## Slide 38: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching
How are these implemented?

## Slide 39: Circuit Switching
(1) src sends a reservation request for 10Mbps to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 40: Circuit Switching
switch
src
dst
Reservation also establishes a “circuit” within a switch

## Slide 41: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 42: Timing in Circuit Switching
time

## Slide 43: Timing in Circuit Switching
time

## Slide 44: Timing in Circuit Switching
time

## Slide 45: Timing in Circuit Switching
time

## Slide 46: Timing in Circuit Switching
time
Circuit establishment

## Slide 47: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer

## Slide 48: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 49: Efficiency in Circuit Switching
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 50: Efficiency in Circuit Switching
Data
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 51: Circuit Switching and Failures
A
B
Circuit switching doesn’t “route around trouble”
Circuit is established
Link Fails along path
Must establish new circuit

## Slide 52: Circuit Switching
Pros
  Predictable performance
  Simple/fast switching (once circuit established)
Cons
  Complexity of circuit setup/teardown
  Inefficient when traffic is bursty (or very short)
  Circuit setup adds delay
  Switch fails  its circuit(s) fails
    Requires new circuit establishment phase

## Slide 53: Packet switching
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 54: Packet switching
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 55: Packet Switching and Failures
A
B
Packet switching “routes around trouble”
Link Fails along path
Route recomputed on the fly

## Slide 56: Packet Switching
Pros
  Efficient use of network resources
  Simpler to implement
  Robust: can “route around trouble” (covered in routing)
Cons
  Unpredictable performance
  Requires buffer management and congestion control

## Slide 57: Packet vs Circuit Switching
Key factors:
  Resiliency: packet switching wins
  Efficiency: packet switching wins (bursty sources)
Internet has chosen packet switching
  Our focus for rest of course
  How can we measure performance of packet switching?

## Slide 58: Performance Metrics
Delay
Loss
Throughput

## Slide 59: Delay
How long does it take to send a packet from its source to destination?

## Slide 60: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 61: Throughput
At what rate is the destination receiving data from the source?

## Slide 62: Today
Focus on delay
Loss and throughput will become relevant in later lectures….

## Slide 63: A network link
Link bandwidth
  Number of bits sent per unit time (bits/sec or bps)
Propagation delay (sometimes called latency)
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time (sent, not recvd)
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 64: Examples of BDP
Same city over a slow link:
  bandwidth: ~100Mbps
  propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  bandwidth: ~10Gbps
  propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 65: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Processing delay
  Queueing delay
First consider transmission, propagation delays
Then queueing delays
Ignore processing delays (tiny in most cases)
due to link properties
due to traffic mix and
switch internals

## Slide 66
transmission
End-to-end delay
propagation
queuing
processing
transmission
propagation
queuing
processing
transmission
propagation

## Slide 67: Transmission Delay
Q: How long does it take to push all the bits of a packet into a link?
A: Packet size / Transmission rate of the link
Example: Packet = 1kb, Rate = 100Mbps
  1000 bits / 100 Mbits per sec = 10-5 sec = 10μsec

## Slide 68: Propagation Delay
Q: How long does it take to move one bit from one end of a link to the other?
A: Link length / Propagation speed of link
  Propagation speed ~ some fraction of speed of light
Example: Length = 30 kilometers
  30 kilometers/3x108 meters per sec = 10-4 sec = 10msec

## Slide 69: Now ask a more practical question
Q: How long does it take for a packet to travel from A to B?
A: The delay combines both transmission and propagation delays
  Perhaps also queueing, but ignore those for now

## Slide 70: Example: 100B packet from A to B
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 71: Example: 100B packet from A to B
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 72: Three cases with 1msec prop. delay
1GB file, 1Gbps link: transmission time dominant
100B packet, 1Gbps link: propagation delay dominant
100B packet, 1Mbps link: transmission ~ propagation
Design differs based on which dominates
  But in the Internet, can’t know in advance!

## Slide 73: Technology Trends
Propagation delay?
  No change
Transmission delay?
  Getting smaller!
Queueing delay?
  Usually smaller
How does this affect applications?
  CDNs work very hard to move data near clients
  Reduces backbone bandwidth requirements
  But also decreases latency
  Google: time is money!

## Slide 74: What Trend Did I Leave Out?
The dominance of video
Very high fraction of traffic is video
Files getting larger
But also many, many small flows…

## Slide 75: The “pipe” view
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 76: The “pipe” view
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 77: The “pipe” view
1Mbps, 10ms (BDP=10,000)
time 
BW 
1Mbps, 10ms (BDP=10,000)
time 
BW 
100b packets
250b packets

## Slide 78: What happens here with on-demand?
What do we do under overload?
Time
Link capacity = 30Mbps
Notes: What we discuss at end of lecture…

## Slide 79: Answer
Packets temporarily buffered (queueing delays)
Or dropped (if buffer overflows)
Let’s talk about queueing for a bit…

## Slide 80: Queueing delay: “pipe” view

## Slide 81: Queueing delay: “pipe” view
No overload!

## Slide 82: Queueing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 83: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 84: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 85: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 86: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 87: Queueing delay: “pipe” view
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts but introduce queueing delay

## Slide 88: Queueing delay: “pipe” view
What about persistent overload?
Will eventually drop packets (“loss”)

## Slide 89: More packet animations….

## Slide 90: The Lifecycle of Packets
Excess Packets
Stored in Buffer
Packet Arriving
at Switch
Packet
Being
Transmitted
Packet Buffer
Link
Packet Currently
Being Transmitted

## Slide 91: The Delays of Their Lives
Queueing
Delay
Transmission
Delay
Propagation Delay is how long it takes
to reach the next switch after transmission
Round-Trip Time (RTT) is the time it takes
a packet to reach the destination and
the response to return to the sender

## Slide 92: Smooth Arrivals = No Queueing Delays

## Slide 93: Bursty Arrivals = Queueing Delays
There is substantial queueing delay even though link is underutilized

## Slide 94: Packet Losses: Buffers Full

## Slide 95: Packet Losses: Corruption

## Slide 96: Queueing Delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  Arrival rate at the queue
  Nature of arriving traffic (bursty or not?)
  Transmission rate of outgoing link

## Slide 97
arrival rate / departure rate
1
Average queuing delay
Notes: This plot shows the average queuing delay experienced by a packet arriving at a buffer,
as a function of this entity here, which is the arrival rate divided by the departure rate.
As this entity approaches 1 (the arrival rate approaches the departure rate),
the average delay goes to infinity.
The important thing to note about this curve is the shape.
When we approach close to this area here, the curve goes up very fast.
This means that small changes in arrival rate can have a dramatic impact on delay.
This is what happens when you are driving in a congested highway.
The smallest disturbance (like one car braking) can significantly increase your delay.
When you design a queuing system, you want it to operate far from that point.

## Slide 98: Basic Queueing Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 99: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Compute A: count packets sent over time
Why do you care?
  Easy to compute L and A, harder to compute W

## Slide 100: Thursday’s lecture….
Layering, principles, the “good stuff”
Read K&R 1.4-1.8 (mostly for context)