## Slide 1: CS 168 Routing Fundamentals
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2: Administrivia
Everyone should have an account
Homework #1 will be posted tomorrow morning
No, I have no control over the waiting list
We have a new TA

## Slide 3: Agenda for Today
Finish up last lecture (Design Goals)
Review the course so far
Fundamentals of Routing

## Slide 4: Internet Design Goals

## Slide 5: David Clark
Wrote a paper in 1988 that tried to capture why the Internet turned out as it did
In particular, it described an ordered list of priorities that informed the design

## Slide 6: Internet Design Goals (Clark ‘88)
Connect existing networks (Kahn’s stated goal)
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability
Notes: Important that his is an ORDERED list.

## Slide 7: #1 Connect Existing Networks
Wanted single protocol that could be used to connect any pair of (existing) networks
The Internet Protocol (IP) is that unifying protocol
  All (existing) networks must be able to implement it
This is where the need for best effort arose….
  And this is where circuit switching died
  Why?

## Slide 8: #2 Robust
Def’n A: As long as network is not partitioned, two hosts should be able to communicate (eventually)
  Must eventually recover from failures
Def’n B: Failures (excepting network partition) should not interfere with endpoint semantics
  Must always isolate endpoints from failures
A: Very successful, not clear how relevant now
  Availability more important than recovering from disaster
B: This notion of robustness is underappreciated
  Key to modularity of Internet

## Slide 9: The Internet Architecture
Layer | Scope | Granularity | Where | Unique?
Application | Host | Data | Host | No
Reliability | Global | Data | Host | No
Network | Global | Packets | Network | Yes
Link | Local | Packets | Network | No
Physical | Local | Bits | Network | No

## Slide 10: The Telephony Architecture
Layer | Scope | Granularity | Where | Unique?
Application | Host | Data | Network And Host | No
Reliability | Global | Data | Network | No
Network | Global | Packets | Network | Yes
Link | Local | Packets | Network | No
Physical | Local | Bits | Network | No

## Slide 11: #3 Types of Delivery Services
Use of the term “delivery services” already implied an application-neutral network
Built lowest common denominator service
  Allow end-based protocols to provide better service
  For instance, turn unreliable service into reliable service
Example: recognition that TCP wasn’t needed (or wanted) by some applications
  Separated TCP from IP, and introduced UDP

## Slide 12: The paradox of the Internet’s design
The goal is to support many applications
These applications have different requirements
Shouldn’t the Internet support them all?
  That is, provide a service the satisfies all of them
  By meeting the most stringent requirements

## Slide 13: What service should Internet support?
Strict delay bounds?
  Some applications require them
Guaranteed delivery?
  Some applications are sensitive to packet drops
No applications mind getting good service
  Why not require Internet support all these guarantees?

## Slide 14: Important life lessons
(1) People (or applications)
Don’t always need what they think they need
Almost never need what we think they need
(2) Flexibility often more important than performance
But typically only in hindsight!
Example: cell phones vs landlines
(3) Architect for flexibility, engineer for performance
Flexibility ensures longevity
Performance requirements are ephemeral

## Slide 15: Applying lessons to Internet
Requiring performance guarantees would limit variety of networks that could attach to Internet
Many applications don’t need these guarantees
And those that do?
  Well, they don’t either (usually) (Why?)
  Tremendous ability to mask drops, delays
And ISPs can work hard to deliver good service without changing the architecture (engineering)

## Slide 16: Bottom Line
The choice of “best-effort” packet switching service is not as obvious as it might seem today
Great vision on the part of the Internet designers
And lucky that they were focused on applications that did not need great service

## Slide 17: #4 Variety of Networks
Incredibly successful!
  Minimal requirements on networks
  No need for reliability, in-order, fixed size packets, etc.
  A result of aiming for lowest common denominator
IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: Wifi, Cellular, ATM, SONET, WDM…

## Slide 18: #5 Decentralized Management
Both a curse and a blessing
  Important for easy deployment
  Makes management hard today
Recent efforts have improved management of individual networks
  But no attempt to manage the Internet as a whole….

## Slide 19: #6 Host Attachment
Clark observes that cost of host attachment may be higher because hosts have to be smart
But the administrative cost of adding hosts is very low, which is probably more important
  Plug-and-play kind of behavior….

## Slide 20: #7 Cost Effective
Cheaper than circuit switching at low end
More expensive than circuit switching at high end
  Why?
Not a bad compromise:
  Cheap where it counts (low-end)
  More expensive for those who can pay….

## Slide 21: #8 Resource Accountability
Failure!

## Slide 22: Internet Motto
We reject kings, presidents, and voting. We believe in rough consensus and running code.”
David Clark

## Slide 23: Real Goals
Build something that works!
Connect existing networks
Robust in face of failures
Support multiple types of delivery services
Accommodate a variety of networks
Allow distributed management
Easy host attachment
Cost effective
Allow resource accountability

## Slide 24: Questions to think about….
What priorities would a commercial design have?
  Probably focus on high-revenue applications
What would the resulting design look like?
  Probably bake some of the application into the network
What goals are missing from this list?
  Suggestions?

## Slide 25: Some of the missing issues
Security
  Resilience to attacks (denial-of-service)
  Endpoint security
  Tracking down misbehaving users
Privacy
Availability
Resource sharing (fairness, etc.)
ISP-level concerns
  Technical issues of interconnection and internal management
  Economic issues of interconnection
  Value flow (who should get paid for these bits?)

## Slide 26: The Course So Far….

## Slide 27: Internet Architecture is an Exercise in Modularity
Modularity led to the basic design decisions
And these design decisions have enabled the Internet to scale in:
  Size
  Speed
  Diversity of technologies
  Diversity of applications
  Diversity of end points

## Slide 28: Decisions and Their Principles
How to break system into modules
  Dictated by Layering
Where modules are implemented
  Dictated by End-to-End Principle
Where state is stored
  Dictated by Fate-Sharing

## Slide 29: Five Layers
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 30: Traditional Courses
Cover each layer in order (as in our textbook)
  Philosophies differ as to top-down vs bottom-up
I prefer to focus on the distinction between
  Fundamental intellectual challenges
  Design/implementation choices in today’s Internet
We will next address fundamental challenges
Later will discuss current designs in each layer

## Slide 31: Which of these tasks are hard?
Application: not a fundamental challenge
  Not general, and not necessarily hard
Reliable transport: a fundamental challenge
  General, and difficult
Global and local packet delivery:
  Local and global packet delivery both require routing
  This is a general and difficult challenge
Physical transfer: not a fundamental challenge
  Not general, and not conceptually difficult

## Slide 32: Two Fundamental Challenges
Routing: guiding packets from source to destination
Reliable delivery: building a reliable transport service on top of best-effort delivery
Other pieces required to build operational networks
  Naming, addressing, congestion control,….
  We will get to those later in the course
But these two are inherent and hard
  Routing: next few lectures
  Reliable transport: lecture after that

## Slide 33: A Few Preliminaries
Before we can study routing, we need to clarify:
  Network Topologies
  Switches/Routers
  Forwarding
  Packets

## Slide 34: Example of Network Graph
Router with 6 attached links
Router with 4 attached links

## Slide 35: A Variety of Networks
ISPs: carriers
  Backbone
  Edge (connecting to customers)
  Border (to other ISPs)
Enterprises: companies, universities
  Core
  Edge (connecting to hosts)
  Border (to outside)
Datacenters: massive collections of machines
  Aggregation and Core
  Top-of-Rack
  Border (to outside)

## Slide 36: UUNET’s North American Network
Notes: Very irregular

## Slide 37: Level3’s American Network (check out their interactive map)

## Slide 38: Enterprise Network
Notes: Not very detailed, couldn’t get a better one….

## Slide 39: Berkeley’s Campus Network

## Slide 40: Partial Datacenter Network
Notes: Only a part of the network, but the takeaway is that the network is very regular, involving levels of hierarchy.

## Slide 41: Switches/Routers
Multiple attached links, often called “ports”
Ports are typically duplex (incoming and outgoing)
  But in this picture will show them separately
  (Don’t confuse this notion of “port” with transport “ports”)
incoming links
outgoing links
Switch

## Slide 42: Forwarding Decisions
When packet arrives, must choose outgoing port
Decision is based on routing state (table) in switch
incoming links
outgoing links
Switch
Consider
packet header
and routing
table

## Slide 43: Forwarding Decisions
Switches and routers make the following mapping:
PacketState + RoutingState  OutgoingPort
Most do so in single transmission time
  Forwarding decisions must be simple
Assume forwarding decisions are deterministic
  Packets with same state always routed to same port

## Slide 44: Packets (at a conceptual level)
Assume packet headers contain:
  Destination ID
  Source ID
  …and perhaps other information
Destination
Identifier
Source
Identifier
Payload
Why include
this?

## Slide 45: Forwarding Decision Dependencies
Must depend on destination
Could also depend on :
  Source: requires n2 state
  Input port: not clear what this buys you
  Other header information: ignore for now
We will focus only on destination-based routing
  But first consider the alternative

## Slide 46: Source/Destination-Based Routing
Paths from two different sources (to same destination) can be very different

## Slide 47: Destination-Based Routing
Paths from two different sources (to same destination) must coincide once they overlap
Notes: Why coincide?

## Slide 48: Destination-Based Routing
Paths to same destination never cross
Once paths to destination meet, they never split
Set of paths to destination create a “delivery tree”
  Must cover every node exactly once
  Only one outgoing arrow at each node
  All nodes have path to destination
Produces Spanning Tree rooted at destination
Notes: You all know what a spanning tree is?

## Slide 49: A “Delivery Tree” for a Destination

## Slide 50: Assume Destination-Based Routing
For rest of lecture (and course)…..

## Slide 51
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
MIT | switch#2
NYU | switch#3
Forwarding Table
111010010
MIT
switch#2
switch#5
switch#3
switch#4

## Slide 52: Forwarding
The act of forwarding in a router:
  Read address from packet’s header
  Search routing state for correct output port
  Send (within router) to correct output port
Forwarding is a local process within a router

## Slide 53
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
MIT | switch#2
NYU | switch#3
Forwarding Table
111010010
MIT
switch#2
switch#5
switch#3
switch#4
switch#1

## Slide 54: Routing
Routing is what computes the routing state
  Also called forwarding state
This is inherently a global process
  How can you know where to send packets without knowing what the overall network looks like?

## Slide 55
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
MIT | switch#2
NYU | switch#3
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Forwarding Table
switch#1
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#6
NYU | switch#1

## Slide 56: Forwarding vs Routing
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Routing: “control plane”
  Computing paths the packets will follow
  Routers talking amongst themselves
  Jointly creating the routing state
Two very different timescales….
  Nanoseconds vs (hopefully) 10s of milliseconds

## Slide 57: Local vs Global View of State
Local routing state is table in a single router
  By itself, the state in a single router can’t be evaluated
  It must be evaluated in terms of the global context
Global state is collection of tables in all routers
  Global state determines which paths packets take
  (Will discuss later where this routing state comes from)

## Slide 58
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
MIT | switch#2
NYU | switch#3
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Forwarding Table
switch#1
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#6
NYU | switch#1

## Slide 59: “Valid” Routing State
Global routing state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
  Valid is my terminology, not standard
Goal of routing protocols: compute valid state
  But how can you tell if routing state if valid?
Need a succinct correctness condition for routing
  Suggestions?
Notes: What could go wrong?

## Slide 60: Necessary and Sufficient Condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing port
  A packet arrives, but the forwarding decision does not yield any outgoing port
A loop is when a packet cycles around the same set of nodes forever

## Slide 61: Packet Hitting Dead End
Packet reaches deadend and stops (and dropped)

## Slide 62: Packet Entering Loop
Packet falls into loop and never reaches destination

## Slide 63
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
MIT | switch#2
NYU | switch#3
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Forwarding Table
switch#1
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Loop!

## Slide 64
to MIT
to UW
to UCB
to NYU
Destination | Next Hop
UCB | switch#4
UW | switch#5
NYU | switch#3
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Forwarding Table
switch#1
Destination | Next Hop
UCB | switch#1
UW | switch#1
MIT | switch#1
NYU | switch#1
Deadend (to MIT)

## Slide 65: Logic Refresher
A if B means B  A
  if B is true, then A is true
A only if B means A  B
  if A is true, then B is true
A if and only if B means: A  B
  If A is true, then B is true
  If B is true, then A is true
To make the statement that A if and only if B, you must prove statements 1 and 2.

## Slide 66: Necessary and Sufficient Condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
Necessary: (only if)
  If routing state valid, then there are no loops/deadends
Sufficient: (if)
  If no loops/deadends, then routing state is valid

## Slide 67: Necessary (“only if”): Easy
If you run into a deadend before hitting destination, you’ll never reach the destination
If you run into a loop, you’ll never reach destination
  With deterministic forwarding, once you loop, you’ll loop forever (assuming routing state is static)
Therefore:
  If routing state valid, then there are no loops/deadends

## Slide 68: Sufficient (“if”): More Subtle
Assume no deadends, no loops
Packet must keep wandering, without repeating
  If ever enter same switch from same port, will loop
  Because forwarding decisions are deterministic
Only a finite number of possible ports for it to visit
  It cannot keep wandering forever without looping
  Must eventually hit destination
Therefore:
  If no loops/deadends, then routing state is valid
Notes: Destination is only safe deadend

## Slide 69: Two Questions
How can we verify given routing state is valid?
How can we produce valid routing state?

## Slide 70: Checking Validity of Routing State
Focus only on a single destination
  Ignore all other routing state
Mark outgoing port with arrow
  There can only be one at each node
Eliminate all links with no arrows
Look at what’s left….
  State is valid if and only if remaining graph is spanning tree rooted at destination

## Slide 71: Example 1

## Slide 72: Pick Destination

## Slide 73: Put Arrows on Outgoing Ports (output ports towards green dot)

## Slide 74: Remove Unused Links
Leaves Spanning Tree: Valid

## Slide 75: Second Example

## Slide 76: Second Example
Is this valid?

## Slide 77: Lesson….
Very easy to check validity of routing state for a particular destination
Deadends are obvious
  Node without outgoing arrow
Loops are obvious
  Disconnected from destination (and rest of graph)

## Slide 78: Two Questions
How can we verify given routing state is valid?
How can we produce valid routing state?

## Slide 79: The “Secret” of Routing
Avoiding deadends is easy
Avoiding loops is hard
  And here we mean persistent loops
The key difference between routing protocols is how they avoid loops!
  Don’t focus on details of mechanisms
  Just ask “how are loops avoided?”
Many different variations of route computations
  But before I tell you how to route….
Notes: Most modern routing research is about how to make the loop-freeness a more fundamental part of the algorithm. In what I’m going to present today, it is only loop-free AFTER convergence. That’s not good enough

## Slide 80: Learn-By-Doing
I need 40 volunteers
If you haven’t participated, this is your chance!

## Slide 81: The Task
Do not look at sheet of paper until I say so
You will have five minutes to complete this task
Each sheet says:
You are node X You are connected to nodes Y,Z
Your job: find route from source (node 1) to destination (node 40) in five minutes

## Slide 82: Ground Rules
You may not:
  Leave your seat (but you can stand)
  Pass your sheet of paper
  Let anyone copy your sheet of paper
You may:
  Ask nearby friends for advice
  Shout to other participants (anything you want)
  Curse your instructor (sotto voce)
You must: Try

## Slide 83: Go!