## Slide 1: CS 168 More Routing
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2: Administrivia
Homework #1 is out: due on the 25th
  Do not be scared by the math
  If you understand the networking content, math will follow
  If you focus only on the math, you are missing the point.
  Come to office hours if you don’t understand

## Slide 3: Today’s Lecture
Valid Routing: Checking and Producing
Review Tuesday’s exercise
Loop avoiding exercise
Learning switches
Link-state routing

## Slide 4: Condition for Valid Routing State
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops

## Slide 5: Two Questions
How can we verify given routing state is valid?
How can we produce valid routing state?

## Slide 6: Checking Validity of Routing State
Focus only on a single destination
  Ignore all other routing state (why can we do this?)
For each node, mark outgoing port with arrow
  There can only be one at each node
Eliminate all links with no arrows
Look at what’s left….
  State is valid if and only if remaining graph is spanning tree rooted at destination
  Spanning tree: tree that touches all nodes

## Slide 7: Example 1

## Slide 8: Pick Destination

## Slide 9: Put Arrows on Outgoing Ports (output ports towards green dot)

## Slide 10: Remove Unused Links
Leaves Spanning Tree: Valid

## Slide 11: Second Example

## Slide 12: Second Example
Is this valid?

## Slide 13: Third Example

## Slide 14: Third Example
Is this valid?

## Slide 15: Lesson….
Very easy to check validity of routing state for a particular destination
Deadends are obvious
  Node without outgoing arrow, can’t be connected to dest.
Loops are obvious
  Disconnected from destination (and rest of graph)

## Slide 16: Two Questions
How can we verify given routing state is valid?
How can we produce valid routing state?

## Slide 17: The “Secret” of Routing
Avoiding deadends is easy
Avoiding loops is hard
  And here we mean persistent loops
The key difference between routing protocols is how they avoid loops!
  Don’t focus on details of mechanisms
  Just ask “how are loops avoided?”
Many different variations of route computations
  We started with an exercise…..
Notes: Most modern routing research is about how to make the loop-freeness a more fundamental part of the algorithm. In what I’m going to present today, it is only loop-free AFTER convergence. That’s not good enough

## Slide 18: Tuesday’s Class Exercise
Your plan of attack?
  Each person announces a neighbor
  Who then gets up and announces another neighbor….
What is this, more formally?
  A random walk!
  With no repeats, which eliminated loops
You produced a path
  But not a shortest path
  Were lucky that the given graph had low connectivity!

## Slide 19
1
16
36
7
25
10
19
5
34
38
29
33
15
39
23
14
9
2
35
11
22
32
26
21
37
3
28
12
30
4
27
20
31
18
24
40
8
17
6
13

## Slide 20: Here is a better approach
Destination stands up (distance 0)
  Announces neighbors (and then sits down)
Neighbors stand up (distance 1)
  They remember who called them to stand
  They announce their neighbors (distance 2)
  And sit down
These neighbors stand up (if haven’t already)
…..and so on, until source stands
At that point, the source can send a packet to the person who called them to stand, and then recursively the packet can reach the destination….
Notes: Let’s try this again!!!

## Slide 21: The Two Tasks of Routing Algorithms
Find a good path
Install the appropriate state in the routers
  So that packets can be forwarded along that path
This algorithm does both…
  When you reach the source, you know you have a path
  By remembering who called you to stand, you know who to route the packet to

## Slide 22: Why Not Stand Up Twice?
Being called a second time means that there is a second (and longer) path to you
  You already contacted your neighbors the first time
  Your distance to destination is based on shorter path
  What if you stood every time your node is called?

## Slide 23: Standing Whenever Called?
You’ll never sit down!
As long as you remember the first person who called you, the state you compute is fine
But the algorithm doesn’t work well, since people never sit down…
  But that’s actually how some real algorithms work…
  Which is ok if communication is pairwise

## Slide 24: Aside
What if you ignored calls from nodes you contacted?
  i.e., you told them to stand, so you ignore their calls
Does this eliminate the problem?

## Slide 25: Shortest-paths = No loops
This algorithm computes shortest paths
And ignores all paths other than shortest paths
Shortest paths cannot contain loops
  Why?
Later, we will discuss other ways of avoiding loops
Now, back to interpret this exercise in two ways

## Slide 26: Interpretation #1
Destination “floods” packet to network
  Flooding: incoming packet sent to all other ports
    Details discussed later….
Everyone records port where first received packet
  Ignore later arrivals of this packet from destination
  These represent longer paths from destination
  Each node learns first hop of shortest path to destination
When the source first learns of path, you are done

## Slide 27: Question
Would this have worked if Source flooded packet?
Would have:
  Delivered packet to destination
  But learned path towards source, not destination
This method would find a path
  Assuming all links symmetric
But would not install appropriate routing state
  How would a node know how to reach destination?

## Slide 28: Learning from Floods
In this interpretation, you are learning from a packet that has been flooded everywhere
  By recording which port first received the packet
  A clean and elegant way to learn paths (to source of pkt)
Why would you use this?
  If you only wanted forwarding state for active nodes
  Or if you wanted to reach nodes you didn’t know about
    Plug-and-play
What would you need to implement this?
  Some way to flood packets (later in lecture)

## Slide 29: Interpretation #2
Routing algorithm computes routes by having routers announce their distance from destination
  If they know it….
The destination announces first
Then the nodes next to the destination announce
  And so on…
Eventually nodes learn next hop of the shortest path to the destination

## Slide 30: Distributed Route Computation
I am one hop away
I am one hop away
I am one hop away
I am two hops away
I am two hops away
I am two hops away
I am two hops away
I am three hops away
I am three hops away
Destination
I am three hops away

## Slide 31: This Distributed Process
Finds a path
  In fact, shortest path
And creates the appropriate routing state
  Forward packet to neighbor who has the shortest path
And tells everyone the length of remaining path

## Slide 32: How Does This Work?
What if people don’t go in order?
  Someone who is three hops away stands up before someone who is two hops away?
Must announce the distance when you stand up
If learn shorter path:
  Computing path: Announce your new distance
  Installing state: Remember only shortest distance

## Slide 33: Interpretations produce same paths
They differ in implementation:
  One learns about routes from flooded data packets
  The other explicitly exchanges routing state
Will return to these two cases (and others) in the rest of our routing material…

## Slide 34: Returning from exercise to lecture
The key difference between routing protocols is how they avoid loops!
So, how can you avoid loops?
Design exercise: for the next five minutes
  Talk to people around you
  Try to design another way to avoid loops
  Think outside the box, don’t just tweak what we just did
  At end of five minutes, I will call on a few groups….
Notes: Most modern routing research is about how to make the loop-freeness a more fundamental part of the algorithm. In what I’m going to present today, it is only loop-free AFTER convergence. That’s not good enough

## Slide 35: Point of Exercise
Not to get the “right answer”!
I want you to think about loop avoidance yourself
  Then the rest of the lecture will make more sense!
Instructions:
  Talk to people around you
  Try to design another way to avoid loops
  Think outside the box, don’t just tweak what we just did
  At end of five minutes, I will call on a few groups….

## Slide 36: Ways to Avoid Loops (Conceptual)
Tree-like topologies
  If the topology has no loops, you can’t create them
  (Unless you are locally stupid!)
Global view
  If I see the entire network when computing paths I can manually avoid loops
Distributed Computation:
  Routes that minimize a reasonable metric
    Why not maximize?
  Computations that show me the path that I’m choosing

## Slide 37: Ways to Avoid Loops (In Practice)
Tree-like topologies
  Learning switches (L2)
Global view
  Link-state and SDN routing
Distributed Computation:
  Minimizing a metric: Distance vector
  Showing path: BGP
  This is essentially the entire routing literature….

## Slide 38: Rest of Lecture
Going down this list….(but won’t finish)

## Slide 39: Easiest Way to Avoid Loops
Use a topology where loops are impossible!
Take arbitrary topology
Build spanning tree
  Ignore all other links
Only one path to destinations on spanning trees
  So don’t have to worry about loops!

## Slide 40: Consider previous graph

## Slide 41: A Spanning Tree

## Slide 42: Another Spanning Tree

## Slide 43: Yet Another Spanning Tree

## Slide 44: Routing on a Spanning Tree
There is only one path from source to destination
How do you find that path?
Why bother? Just send packets along all paths
  No packets will loop, but most will hit deadends
  But one (and exactly one) will reach destination

## Slide 45: Flooding on a Spanning Tree
If you want to send a packet that will reach all nodes, then switches can use the following rule:
  Ignoring all ports not on spanning tree!
Originating switch sends “flood” packet out all ports
When a “flood” packet arrives on one incoming port, send it out all other ports

## Slide 46: Flooding on Spanning Tree

## Slide 47: Flooding on Spanning Tree (Again)

## Slide 48: How Do You Make Spanning Trees?
The Spanning Tree Protocol (STP)
  Invented by Radia Perlman
  Used to link together Ethernets in the early Internet
How does it work?
  Pick lowest ID in network as root
    This is pretty easy…
  Build tree rooted in that node
    Using techniques similar to the class exercise

## Slide 49: An Ode to STP
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
is loop-free connectivity.
A tree that must be sure to span
so packets can reach every LAN.
First, the root must be selected.
By ID, it is elected.
Least-cost paths from root are traced.
In the tree, these paths are placed.
A mesh is made by folks like me,
Then bridges find a spanning tree.

## Slide 50: Flooding on a Spanning Tree
This works because the lack of loops prevents the flooding from cycling back on itself
Eventually all nodes will be covered, exactly once

## Slide 51: But isn’t flooding wasteful?
Yes, but you can watch the packets going by, and learn from that
There is a single path between any two nodes
If node A sees a packet from node B come in on a particular port, what can it conclude?
It knows what port to use to reach B!

## Slide 52: Nodes can “learn” routing tables
Switch can learn how to reach nodes by remembering where flooding packets came from!
If flood packet from Node A entered switch from port 4, then switch uses port 4 to reach Node A
This is just interpretation #1 of our exercise….

## Slide 53: Learning from Flood Packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 54: Node B Responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 55: General Approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded
The decision to flood or not is done on a switch-by-switch basis….

## Slide 56: Self-Learning Switch
When a packet arrives
Inspect source ID, associate with incoming port
Store mapping in the switch table
Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 57: Self Learning: Handling Misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response will teach switch about that destination
A
B
C
D

## Slide 58: General Rule
When switch receives a packet:
index the switch table using destination ID
if entry found for destination {
if dest on port from which packet arrived then drop packet
else forward packet on port indicated
}
else flood
forward on all but the interface
on which the frame arrived
Why do this?

## Slide 59: Summary of Learning Approach
Avoids loop by restricting to spanning tree
This makes flooding possible
Flooding allows packet to reach destination
  “Plug and play”
And in the process switches learn how to reach source of flood
No explicit route “computation”

## Slide 60: Weaknesses of This Approach?
Requires loop-free topology (Spanning Tree)
  Must eliminate many links from physical topology
  Reducing bisection bandwidth (important in datacenters)
  Very little control over paths (traffic engineering)
Slow to react to failures
  Tree must be recomputed
Slow to react to host movement
  Entries must time out
Spanning Trees suck (just ask an operator)

## Slide 61: Murphy’s Research (AXE)
Do flooding without a spanning tree
  By having routers detect duplicates
Eliminates most weaknesses of this approach
  No need to eliminate links
  Can recover from failures immediately
  ….
This is why we do research….

## Slide 62: Murphy’s Diss Track
I think that I shall never see
A structure more wasteful than a tree.
Most links remain idle and unused
while others are overloaded and abused.
And with each failure comes disruption
caused by the ensuing tree construction.
Thus, L2 must discard its spanner,
requiring flooding in a different manner.
AXE avoids the tree’s fragility and waste
with routers that detect when packets duplicate.
Notes: Our version of Drake vs Meek Mill