## Slide 1: CS 168 Addressing
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Agenda for Today
Review of IP:
  Quick review of fragmentation
  Discussion of IPv4 vs IPv6
Q&A on Project 1
IP Addressing
  to be continued on Tuesday

## Slide 4: Why do I care about fragmentation?
I don’t. Not one whit.
But it is a good exercise in header engineering
  They could have done this stupidly, but didn’t
And it gives you a chance to show you understand how the various header fields work….

## Slide 5: Example of fragmentation
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
A 4000 byte packet crosses a link w/ MTU=1500B
IP header

## Slide 6: A few considerations
Which layer reassembles?
Where to reassemble?
Fragments can get lost
Fragments can follow different paths
Fragments can get fragmented again

## Slide 7: Why reassemble at IP layer?
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
IP header
20
TCP
TCP
TCP
HTTP
HTTP
HTTP
Must reassemble before sending the packet to the higher layers!

## Slide 8: Where Should Reassembly Happen?
Answer 1: router R2
1000
500
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000

## Slide 9: Where should Reassembly Happen?
Answer 2: end-host B (receiver)
500
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000

## Slide 10: Where should reassembly occur?
Classic case of E2E principle
At next-hop router imposes burden on network
  complicated reassembly algorithm
  must hold onto fragments/state
Any other router may not work
  Fragments may take different paths
Little benefit, large cost for network reassembly
Hence, reassembly is done at the destination

## Slide 11: Reassembly: what fields?
Need a way to identify fragments of the packet
   introduce an identifier
Fragments get reordered?
   need some form of sequence number or offset?
Sequence numbers / offset
  How do I know when I have them all? (need max seq# / flag)
  What if a fragment gets re-fragmented?

## Slide 12: IPv4’s fragmentation fields
Identifier: which fragments belong together
Flags:
  Reserved: ignore
  DF: don’t fragment (why?)
    may trigger error message back to sender
  MF: more fragments coming
Offset: portion of original payload in this fragment
  in 8-byte units

## Slide 13: Why This Works
Fragment without MF set (last fragment)
  Tells host which are the last bits bits in datagram
All other fragments fill in holes in datagram
  Can be place by the offset
Can tell when holes are filled, regardless of order

## Slide 14: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 15: Example of Fragmentation
Suppose we have a 4000 byte datagram sent from host 1.2.3.4 to host 3.4.5.6 …
… and it traverses a link that limits datagrams to 1,500 bytes
Version
4
Header
Length
5
Type of Service
0
Total Length: 4000
Identification: 56273
R/D/M
0/0/0
Fragment Offset: 0
TTL
127
Protocol
6
Checksum: 44019
Source Address: 1.2.3.4
Destination Address: 3.4.5.6
(3980 more bytes here)

## Slide 16: Example of Fragmentation (con’t)
Datagram split into 3 pieces
Example:
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320

## Slide 17: Example of Fragmentation, con’t
Datagram split into 3 pieces. Possible first piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1500
Identification: 56273
R/D/M
0/0/1
Fragment Offset: 0
TTL
127
Protocol
6
Checksum: xxx
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 18: Example of Fragmentation, con’t
Possible second piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1220
Identification: 56273
R/D/M
0/0/1
Fragment Offset: 185
(185 * 8 = 1480)
TTL
127
Protocol
6
Checksum: yyy
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 19: Example of Fragmentation, con’t
Possible third piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1320
Identification: 56273
R/D/M
0/0/0
Fragment Offset: 335
(335 * 8 = 2680)
TTL
127
Protocol
6
Checksum: zzz
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 20: IPv6

## Slide 21: IPv6
Motivated (prematurely) by address exhaustion
  Addresses four times as big
Steve Deering focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
  “Spring Cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 22: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 23: Summary of Changes
Eliminated fragmentation (why?)
Eliminated header length (why?)
Eliminated checksum (why?)
New options mechanism (next header) (why?)
Expanded addresses (why?)
Added Flow Label (why?)

## Slide 24: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 25: Philosophy of Changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation
  Eliminated checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header approach)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 26: Comparison of Design Philosophy
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
To Destination and Back (expanded)
Deal with Problems (greatly reduced)
Read Correctly (reduced)
Special Handling (similar)

## Slide 27: Q&A on Project 1

## Slide 28: IP Addressing

## Slide 29: Basics of Addressing

## Slide 30: Have covered everything but addresses!
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 31: Use of Addresses
Used by routers to forward packets to destination
Very poor identifier (forget about this use for now)
Focus on use in forwarding

## Slide 32: Forwarding vs Routing
Routing: “control plane”
  Computing paths the packets will follow
  Distributed protocol leads to state at each router
Forwarding: “data plane”
  Directing a data packet to an outgoing link
  Individual router using routing state
Two very different timescales….
  Forwarding: single packet transmission times: μs
  Routing: can be seconds

## Slide 33: Designing an Addressing Scheme
Must support very fast forwarding
  Relatively simple lookup
  Relatively small routing tables
Routing state must be scalably computable
  Cannot involve massive exchanges of state

## Slide 34: Current IP Addressing
Reflects series of necessary hacks
  Necessary to survive, but not pretty…
No one would design such a system from scratch
Simple to design a much better scheme
  Which you will do later in the year!

## Slide 35: Layer 2 Addressing
Typically uses MAC addresses
Unique numbers burned into interface cards
  Random string of bits
  No location information
Local area networks route on these “flat” addresses
Why can’t we use this approach for IP?

## Slide 36: Layer 2 is Local, but Layer 3 is Global!
Would have entry for every device in the world
  Must keep track of their location individually
  Update table whenever they moved!
Leads to large routing tables (~108 or more)
Leads to unscalable routing algorithms
  Global messages whenever laptop moves

## Slide 37: Addressing Goal: Scalable Routing
State: Limited amount of routing state (i.e., table)
  Much less than the number of hosts
Churn: Limited rate of change in routing tables
  Traffic, inconsistencies, complexity
Aggregation crucial for both
(use single entry to cover many addresses)

## Slide 38: Aggregation only works if….
Groups of addresses require same forwarding
These groups are contiguous in address space
These groups are relatively stable
Few enough groups to make forwarding easy

## Slide 39: Example where aggregation works…
1-4 are on left
5-8 are on right
1
3
4
2
A
B
C
6
5
8
7

## Slide 40: Why Is Aggregation Nontrivial?
Mobility: laptops, cellphones, etc.
Multihoming: Many entities have two or more ISPs
Institutional renumbering hard

## Slide 41: Basic Design

## Slide 42: Design Questions
What should an address be associated with?
  Telephone network is an ambiguous model
  Landlines: number refers to location (hard to move)
  Cell phones: number refers to handset (easily movable)
What structure should addresses have? What are the implications of that structure?
Who determines who gets which addresses in the global Internet?

## Slide 43: IP Addresses (IPv4)
Unique 32-bit number associated with an interface
  on a host, on a router, … connect to ports, links, etc.
  Association can be long-term or short-term
Use dotted-quad notation, e.g., 12.34.158.5:
00001100
00100010
10011110
00000101
12
34
158
5

## Slide 44: Routers in the Network
Routers connect links and networks together
Must forward packets towards destination
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
Router

## Slide 45: Forwarding Table Plays Crucial Role
Table maps IP addresses into output interfaces
Forwards packets based on destination address
…
…
3
1.2.3.6
1
1.2.3.5
1
2
1.2.3.5
1.2.3.4
1.2.3.4
2

## Slide 46: Scalability Challenge
Suppose hosts have random addresses
  Then routers would need a separate entry for each host
  Far too much state to hold in each router
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table
Notes: Churn, not size….

## Slide 47: Two Universal Tricks in CS
When you need more flexibility, you add…
  A layer of indirection
When you need more scalability, you impose…
  A hierarchical structure

## Slide 48: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 94704
  Street: Center Street
  Building on street: 1947
  Location in building: Suite 600
  Name of occupant: Scott Shenker
Forwarding the U.S. mail
  Deliver letter to the post office in the zip code
  Assign letter to mailperson covering the street
  Drop letter into mailbox for the building/room
  Give letter to the appropriate person
???

## Slide 49: Who Knows What?
Does anyone in the US Mail system know where every house is?
Separate routing tables at each level of hierarchy
  Each of manageable scale

## Slide 50: Hierarchical Structure
The Internet is an “inter-network”
  Used to connect networks together, not hosts
Forms a natural two-level hierarchy:
  WAN delivers to the right LAN (i.e., deliver to zip code)
  LAN delivers to the right host (i.e., deliver to house)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network
WAN = Wide Area Network

## Slide 51: Hierarchical Addressing
Prefix is network address: suffix is host address
12.34.158.0/23 is a 23-bit prefix with 29 addresses
  Terminology: “Slash 23”
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 52: IP Address and a 23-bit Subnet Mask
00001100
00100010
10011110
00000101
12
34
158
5
11111111
11111111
11111110
00000000
255
255
254
0
Address
Mask

## Slide 53: Scalability Improved
Number nearby hosts with same prefix
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
Notes: What are the routing entries?

## Slide 54: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 55: “Subnet” Terminology
Think of LANs as special case of “subnets”
  Subnet is region without routers containing addresses within the “subnet mask”
  Could be a link, or LAN
Textbook has an operational definition of subnet
  Remove all interfaces from hosts, routers
  The regions that remain connected are subnets
Subnets are the lowest level of aggregation
  No routers needed within a subnet
  But you might have switches (L2)

## Slide 56: History of Internet Addressing
Always dotted-quad notation
Always network/host address split (subnets)
But nature of that split has changed over time
How did we arrive at our current addressing scheme?

## Slide 57: Original Internet Addresses
First eight bits: network address (/8)
Last 24 bits: host address
Assumed 256 networks were more than enough!

## Slide 58: Nice Features
Transit routers looked at what portion of address?
  Network
That portion of address space was flat
  No need for hierarchy with 256 entries
Rest of address only relevant on host’s network
But did not provide for enough networks
  Ubiquity of ethernet not foreseen

## Slide 59: Next Design: Classful Addressing
  Class A: if first byte in [0..127]  assume /8 (top bit = 0)
    Very large blocks (e.g., MIT has 18.0.0.0/8)
  Class B: first byte in [128..191]  assume /16 (top bits = 10)
    Large blocks (e.g,. UCB has 128.32.0.0/16)
  Class C: [192..223]  assume /24 (top bits = 110)
    Small blocks (e.g., ICIR has 192.150.187.0/24)
    (My house used to have a /25)
0*******
********
********
********
10******
********
********
********
110*****
********
********
********
126 nets
~16M hosts
~16K nets
~65K hosts
~2M nets
254 hosts

## Slide 60: Classful Addressing (cont’d)
  Class D: [224..239] (top bits 1110)
    Multicast groups
  Class E: [240..255] (top bits 11110)
    Reserved for future use
1110****
********
********
********
11110***
********
********
********
Multicast
Experimental

## Slide 61: What is wrong with classful?
Only comes in 3 sizes
Routers may need state for many class C’s (/24s)
Wasted address space

## Slide 62: Today’s Addressing: CIDR
CIDR = Classless Interdomain Routing
Flexible division between network and host addresses
Must specify both address and mask
  Clarifies where boundary between addresses lies
  Classful addressing communicate this with first few bits
  CIDR requires explicit mask
Mask carried in routing algorithm
  Not implicitly carried in address

## Slide 63: CIDR Addressing
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network.
Network number = IP address + Mask
Written as 12.4.0.0/15 or 12.4/15

## Slide 64: Classful vs. Classless addresses
Example: an organization needs 500 addresses.
  A single class C address not enough (254 hosts).
  Instead a class B address is allocated. (~65K hosts)
  That’s overkill, a huge waste!
CIDR allows an arbitrary prefix-suffix boundary
  Hence, organization allocated a single /23 address (equivalent of 2 class C’s)
Maximum waste: 50%

## Slide 65: CIDR: Hierarchal Address Allocation
Prefixes are key to Internet scalability
  Addresses allocated in contiguous chunks (prefixes)
  Routing protocols and packet forwarding based on prefixes
  Recursively break down chunks as get closer to host
12.0.0.0/8
12.0.0.0/15
12.253.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
12.3.0.0/22
12.3.4.0/24
:
:
12.3.254.0/23
12.253.0.0/19
12.253.32.0/19
12.253.64.0/19
12.253.64.108/30
12.253.96.0/18
12.253.128.0/17
:
:
:
:

## Slide 66: Allocation Done Hierarchically
Internet Corporation for Assigned Names and Numbers (ICANN) gives large blocks to…
  Regional Internet Registries, such as the American Registry for Internet Names (ARIN), which give blocks to…
Large institutions (ISPs), which give addresses to…
Individuals and smaller institutions
FAKE Example:
ICANN  ARIN  AT&T  UCB  EECS

## Slide 67: FAKE Example in More Detail
ICANN gives ARIN several /8s
ARIN gives AT&T one /8, 12.0/8
  Network Prefix: 00001100
AT&T gives UCB a /16, 12.197/16
  Network Prefix: 0000110011000101
UCB gives EECS a /24, 12.197.45/24
  Network Prefix: 000011001100010100101101
EECS gives me a specific address 12.197.45.23
  Address: 00001100110001010010110100010111

## Slide 68: IP addressing  scalable routing?
Hierarchical address allocation only helps routing scalability if allocation matches topological hierarchy

## Slide 69: Scalability: Address Aggregation
Provider is given 201.10.0.0/21 (201.10.0.x .. 201.10.7.x)
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider
Routers in the rest of the Internet just need to know how to reach 201.10.0.0/21. The provider can direct the IP packets to the appropriate customer.

## Slide 70: Aggregation Not Always Possible
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homed customer with 201.10.6.0/23 has two providers. Other parts of the Internet need to know how to reach these destinations through both providers.
 /23 route must be globally visible

## Slide 71: IP addressing  scalable routing?
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.c.*.* is this way
a.b.*.* is this way

## Slide 72: IP addressing  scalable routing?
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
Can add new hosts/networks without updating
the routing entries at France Telecom
foo.com a.d.0.0/16

## Slide 73: IP addressing  scalable routing?
AT&T a.0.0.0/8
LBL a.b.0.0/16
UCB a.c.0.0/16
ESNet
ESNet must maintain routing entries for both a.*.*.* and a.c.*.*

## Slide 74: IP addressing  scalable routing?
Hierarchical address allocation helps routing scalability if allocation matches topological hierarchy
Problem: may not be able to aggregate addresses for “multi-homed” networks
Two competing forces in scalable routing
  aggregation reduces number of routing entries
  multi-homing increases number of entries

## Slide 75: Growth in Routed Prefixes (1989-2005)
Initial growth super-linear; no aggregation
Advent of CIDR allows aggregation: linear growth
Internet boom: multihoming drives superlinear growth
Dot-com implosion; Internet bubble bursts
Back in business

## Slide 76: Same Table, Extended to Present
Stock Market
Crash of 2008
What Happened Here?
Linear growth
Superlinear growth

## Slide 77: Summary of Addressing
Hierarchical addressing
  Critical for scalable system
  Don’t require everyone to know everyone else
  Reduces amount of updating when something changes
Non-uniform hierarchy
  Useful for heterogeneous networks of different sizes
  Class-based addressing was far too coarse
  Classless InterDomain Routing (CIDR) more flexible
But how do you forward on these addresses?