## Slide 1: CS 168 Forwarding
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Announcements
Project news:
  Autograding every 12 hours……
  Autograder is not a substitute for your own testing
  Murphy will answer questions tonight in Soda 420
  And right after announcements
HW2 will be released tonight
Grading of HW1 essentially done, need to review

## Slide 4: Question
We are considering offering a CS194 that would cover three or four networking topics in a project-oriented fashion.
  Security/censorship, new architectures, wireless,…
It would be taught by a combination of professors (Sylvia Ratnasamy and myself) and people who actually build real systems
How many of you are interested in taking this?

## Slide 5: And now, the AXE-man himself….

## Slide 6: Where Are We
Context (History, Goals, Principles, etc.)
  Done
Fundamental Challenges (Routing, Reliable Trans.)
  Done
Today’s Internet
  IP: Done
  Addressing: Done
  Using Addresses: Today and Thursday
  TCP, DNS, Web,….following few lectures
  Midterm

## Slide 7: Review of Addressing
  Notation: dotted quad (set of four 8-bit numbers)
  16.45.231.117=00010000|00101101|11100111|01110101
Structure: (prefix, suffix)
  Network component (prefix)
  Host component (suffix)
  Use “slash” notation to denote the network component
    /8 means prefix is first 8 bits
Routers only look at network component
  L2 networks mostly look at host component (Thursday)

## Slide 8: History of Addressing Schemes
Original: prefix of length 8 (all addresses in /8s)
Classful: opening bits determined length of prefix
  0 meant /8
  10 meant /16
  110 meant /24
  1110 meant mcast
  1111 meant experimental
Classless (CIDR): explicit mask defines prefix

## Slide 9: CIDR Addressing
IP Address : 12.4.2.1 IP Mask: 255.254.0.0
00001100
00000100
00000010
00000001
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network location
Address + Mask
Notes: What is slash notation for this prefix?

## Slide 10: CIDR Prefixes
Prefix: 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Use two 32-bit numbers to represent a network prefix
Address + Mask
Written as 12.4.0.0/15 or 12.4/15
Notes: What is slash notation for this prefix?

## Slide 11: Using Addresses
How can you aggregate them? (or not)
How can you use them to forward packets?
  In L3
  In L2
How can you dynamically allocate them?
How can you dynamically share them?

## Slide 12: Using Addresses (Today)
How can you aggregate them? (or not)
How can you use them to forward packets?
  In L3
  In L2
How can you dynamically allocate them?
How can you dynamically share them?

## Slide 13: Aggregation (and not)

## Slide 14: Scalability via Address Aggregation
Provider is given 201.10.0.0/21 (201.10.0.x .. 201.10.7.x)
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider
Routers in the rest of the Internet just need to know how to reach 201.10.0.0/21. The provider can direct the IP packets to the appropriate customer.
Each customer
given smaller prefix

## Slide 15: Global Picture
201.10.0/21Port 1
201.11.0/21Port 2
202/8 Port 4
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP
Only /21 listed in core
/22, /23, /24 only listed in ISP’s router
Notes: If adfertised separtely, would have to change whenever prefixes changed. Added new customer, split old one….

## Slide 16: Prefix Aggregation
Original Prefix:
201.10.0/21=11001001|00001010|00000***|*******
Subprefixes: (disjoint coverage of original prefix)
201.10.0/22=11001001|00001010|000000**|*******
201.10.4/24=11001001|00001010|00000100|*******
201.10.5/24=11001001|00001010|00000101|*******
201.10.6/23=11001001|00001010|0000011*|*******

## Slide 17: Aggregation Not Always Possible
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
Multi-homed customer with 201.10.6.0/23 has two providers. Other parts of the Internet need to know how to reach these destinations through both providers.
 /23 route must be globally visible
Notes: What does core route do now????

## Slide 18: Multihoming Global Picture
201.10.0/21Port 1
201.10.6/23Port ?
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
(1) Which ISP does core send 201.10.6/23 to?
It depends…..
If 201.10.6/23  Port 1 no need to list separately
If 201.10.6/23  Port 2 must list separately
Which raises two questions….

## Slide 19: Addresses Advertised in Two Places?
Provider 1 and Provider 2 both advertise prefix
  That is, they both claim they can reach prefix
What problems does this cause?
  None, in terms of basic connectivity!
DV: routers often offered two paths to destination
  Pick the shorter path
For interdomain routing, other factors matter:
  Policy, nature of commercial relationship, prefix length
We will return to this example….
  Focus now on multihoming as impediment to aggregation

## Slide 20: Multihoming Global Picture
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
(2) What if we have contradictory entries in routing table?

## Slide 21: What’s the Problem?
Packets in 201.10.6/23 match two conflicting entries!
  Every address in 201.10.6/23 is also in 201.10.0/21
Which entry do we use?
We will answer this after a digression into forwarding
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..

## Slide 22: Forwarding

## Slide 23: Networks and routers
AT&T
BBN
NYU
UCB
core
core
edge (ISP)
edge (enterprise)
home, small business
Notes: Bunch of different kinds of routers: small for homes, routers that connect different ISPs or ISPs to enterprises (edge)

## Slide 24: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Processes packets on their way in
Processes packets before they leave
Transfers packets from input to output ports
Input and Output for the same port are on one physical linecard

## Slide 25: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
(1) Implement IGP and BGP protocols; compute routing tables
(2) Push forwarding tables to the line cards

## Slide 26: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)
Constitutes the data plane
Constitutes the control plane
Notes: Control plane: software. Makes decisions over long time horizons.
Data plane: mostly hardware. A decision for each packet.

## Slide 27: Input Linecards: Tasks
Receive incoming packets (physical layer stuff)
Update the IP header (which fields?)
  TTL, Checksum, Options (maybe), Fragment (maybe)
Lookup the output port for the destination IP address
Queue the packet at the switch fabric
Version
Header
Length
Type of Service
(TOS)
Total Length (Bytes)
16-bit Identification
Flags
Fragment Offset
Time to
Live (TTL)
Protocol
Header Checksum
Source IP Address
Destination IP Address
Options (if any)
Payload
Notes: Next: one particular part of the functionality: how to determine the output port for the destination IP address

## Slide 28: Challenge: speed!
100B packets @ 40Gbps  packet every 20 nano secs!
Typically implemented with specialized hardware
  ASICs, specialized “network processors” (return to later)
  “exception” processing often done at control processor

## Slide 29: Forwarding Table Plays Crucial Role
Table maps IP addresses into output interfaces
Forwards packets based on destination address
…
…
3
1.2.3.6
1
1.2.3.5
1
2
1.2.3.5
1.2.3.4
1.2.3.4
2

## Slide 30: Looking up the output port
Upon receiving a packet
  Inspect the destination IP address in the header
  Index into the forwarding table
  If no match, select the default route
  Forward packet out appropriate interface
Default route
  Configured to cover cases where no matches
  Allows small tables at edge (w/o routing algorithms)
    if it isn’t on my subnet, send it to my ISP

## Slide 31: Scaling the Lookup
One entry for each address  4 billion entries!
For scalability, addresses must be aggregated
But CIDR aggregation makes lookup harder
Notes: How does a router determine which output port for the packet!

## Slide 32: Efficient Packet Lookup

## Slide 33: Lookup with Original or Classful
Early bits in address specify mask
  Class A [0]: /8 (or all addresses in original addressing)
  Class B [10]: /16
  Class C [110]: /24
Can find exact match in forwarding table
  Use prefix as index into hash table
  Each prefix is in one and only one routing entry
This is easy and fast
  Single hash lookup

## Slide 34: Why won’t this work for CIDR?
What’s the network prefix in this address?
11001001 10001111 00000101 11010010
In CIDR, packet can’t tell you network address
  So how do you know which routing entry to use?

## Slide 35: Example #1: Provider w/ 4 Customers
Prefix | Port
201.143.0.0/22 | Port 1
201.143.4.0.0/24 | Port 2
201.143.5.0.0/24 | Port 3
201.143.6.0/23 | Port 4
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Provider
Port 1
Port 2
Port 3
Port 4

## Slide 36: Finding the Match (at ISP’s Router)
No address matches more than one prefix
  But can’t easily find match
Consider 11001001 10001111 0000010111010010
  First 21 bits match 4 partial prefixes
  First 22 bits match 3 partial prefixes
  First 23 bits match 2 partial prefixes
  First 24 bits match exactly one full prefix
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23

## Slide 37: Finding Match Efficiently
Testing each entry to find a match scales poorly
  Roughly (number of entries) × (number of bits)
Must leverage tree structure of binary strings
  Set up tree-like data structure
Return to example:
Prefix | Port
1100100110001111000000********** | 1
110010011000111100000100******** | 2
110010011000111100000101******** | 3
11001001100011110000011********* | 4
Prefix | Port
1100100110001111000000********** | 1
110010011000111100000100******** | 2
110010011000111100000101******** | 3
11001001100011110000011********* | 4

## Slide 38: Consider four three-bit prefixes
Just focusing on the bits where all the action is….
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4

## Slide 39: Tree Structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
Notes: Many more advanced techniques for this….

## Slide 40: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Many more advanced techniques for this….

## Slide 41: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P3
P4
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Many more advanced techniques for this….

## Slide 42: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P3
P4
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Example: 010  P1
Example: 110  P4
Example: 100  P3
Example: 101  P2
Notes: Many more advanced techniques for this….

## Slide 43: This Example is Too Simple
The prefixes don’t overlap
  This limits the degree of aggregation
The goal is smaller routing tables
But if the prefixes don’t overlap, we may need to list many prefixes in order to specify all routers
What if 11111111111111111111111111111111 went to port 2, and all other addresses went to port 1?
  How many prefixes would we need in routing table?

## Slide 44: Many Routing Entries…
11111111111111111111111111111111  port 2
11111111111111111111111111111110  port 1
1111111111111111111111111111110/31 port 1
111111111111111111111111111110/30  port 1
11111111111111111111111111110/29  port 1
1111111111111111111111111110/28  port 1
…..

## Slide 45: Avoiding Overlaps is Wasteful
But with overlaps come contradictions….

## Slide 46: Return to Multihoming Global Picture
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
(2) What if we have contradictory entries in routing table?

## Slide 47: We have now returned to problem…
Packets in 201.10.6/23 match two conflicting entries!
  Every address in 201.10.6/23 is also in 201.10.0/21
Which do we take?
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..

## Slide 48: Two ways to write the routing table
Compact but contradictory:
Nonoverlapping (and clear) but verbose:
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 1
201.10.5/24Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
Notes: 201.143.4.0.0/24
201.143.5.0.0/24
201.143.6.0/23

## Slide 49: Change old tree-walking example…
From case where prefixes go to different locations
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4

## Slide 50: …to this
Several of the unique prefixes go to same port
0**  Port 1
100  Port 2
101  Port 1
11*  Port 1
How can we represent this more compactly?

## Slide 51: Prefix Tree
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P1
P1
0**  Port 1
100  Port 2
101  Port 1
11*  Port 1
Notes: Many more advanced techniques for this….

## Slide 52: More Compact Representation
10*
100
0
1**
0
***
1
P2
P1
Record port associated with first match, and only over-ride when it matches another prefix during walk down tree
This is longest prefix match (LPM)
If you ever leave path, you are done, last matched prefix is answer
Notes: Many more advanced techniques for this….

## Slide 53: Longest Prefix Match
***  Port 1
100  Port 2
If address matches both, then take longest match
If address matches no prefix, take default route

## Slide 54: Longest Prefix Match Representation
201.143.0.0/21  Port 1
201.143.4.0/24  Port 2
If address matches both, then take longest match
If address matches neither, take default path

## Slide 55: We Use LPM Every Day…..
“Everyone go outside to play….
…except for John, who has to stay inside…”
We routinely insert an “except” whenever we make a general statement and then a contradictory specific statement
Point: we would never explicitly list the members of the class, but instead use the term for the aggregate and then specify the exceptions

## Slide 56: Example #2: Aggregating Customers
Prefix | Port
201.143.0/21 | Provider 1
201.144.0/21 | Provider 2
201.144.0.0/21
201.144.0.0/22
201.144.4.0/24
201.144.5.0/24
201.144.6.0/23
Provider 2
201.143.0.0/21
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Provider 1

## Slide 57: Global Picture
201.143.0/21Port 1
201.144.0/21Port 2
201.145.0/21Port 3
……………..
201.143.0/22Port 1
201.143.4/24Port 2
201.143.5/24Port 3
201.143.6/23Port 4
Router in Internet Core
Router in ISP1
Router in ISP2
201.144.0/22Port 1
201.144.4/24Port 2
201.144.5/24Port 3
201.144.6/23Port 4

## Slide 58: Example #3: Complications
201.144.0.0/21
201.144.0.0/22
201.144.4.0/24
201.144.5.0/24
201.144.6.0/23
Provider 2
201.143.0.0/21
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Provider 1
Forwarding table more complicated when addressing is non-topological
Notes: What does core router do now?

## Slide 59: With nonoverlapping entries..
201.143.0/22Port 1
201.143.4/24Port 1
201.144.4/24Port 1
201.143.6/23Port 1
201.144.0/22Port 2
201.144.5/24Port 2
201.143.5/24Port 2
201.144.6/23Port 2
……………..
201.143.0/22Port 1
201.143.4/24Port 2
201.144.4/24Port 3
201.143.6/23Port 4
Router in Internet Core
Router in ISP1
Router in ISP2
201.144.0/22Port 1
201.144.5/24Port 2
201.143.5/24Port 3
201.144.6/23Port 4

## Slide 60: Matching disjoint prefixes
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
11001001
10010000
000000−−
−−−−−−−
11001001
10010000
00000100
−−−−−−−
11001001
10010000
00000101
−−−−−−−
11001001
10010000
0000011−
−−−−−−−
If match any of these prefixes, go to Provider 1
If match any of these prefixes, go to Provider 2
Notes: No address will match more than one of these prefixes

## Slide 61: Focusing Only on Crucial Bits
1
0
1
0
1
0
1
Prefix destined for Provider 1
Prefix destined for Provider 2
No packet will match more than one prefix
All paths reach a unique prefix
Notes: Many more advanced techniques for this….

## Slide 62: More Compact Representation
0
Prefix destined for Provider 1
Prefix destined for Provider 2
Notes: Many more advanced techniques for this….

## Slide 63: Longest Prefix Match
11001001
10001111
00000−−−
−−−−−−−
Provider 1
201.143.0.0/21
Arriving packet: 11001001 10010000 00000101 01101101
New Arriving packet:
11001001 10010000 00000100 01101101
11001001
10001111
00000101
−−−−−−−
11001001
10010000
00000−−−
−−−−−−−
11001001
10010000
00000100
−−−−−−−
Provider 2
201.144.0.0/21
201.144.4.0/24
201.143.5.0/24

## Slide 64: Return to multihoming example
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2

## Slide 65: Global Picture with Multihoming
201.10.0/21Port 1
201.10.6/23Port 2
201.11.0/21Port 3
……………..
201.10.0/22Port 1
201.10.4/24Port 2
201.10.5/24Port 3
201.10.6/23Port 4
Router in Internet Core
Router in ISP1
201.10.6/23Port 1
201.11.0/21Port 2
201.12.0/21Port 3
201.13.0/21Port 4
Router in ISP2
Which ISP does core send 201.10.6/23 to?
LPM says ISP2…..
Need explicit decisions about prefix granularity
ISP1 might also advertise specific prefix

## Slide 66: LPM in real routers
Real routers use far more advanced/complex solutions than the approaches I just described
  but what we discussed is their starting point
With many heuristics and optimizations that leverage real-world patterns
  Some destinations more popular than others
  Some ports lead to more destinations
  Typical prefix granularities

## Slide 67: Forwarding Summary
Nontrivial to find matches in CIDR
  Because can’t tell where network address ends
  Must walk down bit-by-bit
LPM decreases size of routing table
  Reducing memory consumption

## Slide 68: Conceptual Problems with IP Addressing

## Slide 69: What’s Wrong with IP Addressing?
Multihoming not naturally supported
  Causes aggregation problems
Forwarding hard
  LPM is much harder than exact match
No binding to identity (spoofing, etc.) [discuss later]
Scarce (IPv6 solves this)
…..

## Slide 70: Design Exercise
Design better addressing scheme
Take five minutes
Work in groups
Solve aggregation, multihoming, lookup
  Don’t worry about the other issues
  And don’t overthink this….

## Slide 71
Ssssshhhhhhhhhhhhhhh

## Slide 72: Simple proposal for addressing
Back to the future!
  Return to original IP addressing scheme (mostly)
Explicit separation between
  Network addresses (domain, subdomain, etc.)
  Host address
And can add layers of network addresses
Examples:
  N:H
  Na:Nb:H

## Slide 73: Advantages
Multihoming natural: host is both N1:H and N2:H
Aggregation is explicit
  If you want to aggregate N1, N2 into N use
    N:N1 and N:N2 as addresses
Routing is exact match (much easier) on N
  And when there is a stack of network addresses…
  Use “deepest match” not longest match
  And this is merely optimization, not correctness issue

## Slide 74: Why Explicit Aggregation?
Can aggregate any two network addresses
  Rule: to use N:M, then N must know how to route to M
No need for numbering and topology to be tied
  Network numbers can have cryptographic significance
Hierarchy of net addresses can use “next header”
  So header remains fixed length….