## Slide 1: CS 168 Protocol Support for Forwarding
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Last Lecture
Covered how to:
  Aggregate IP addresses
  Forward IP addresses using LPM
    Smaller routing tables
However, routers focus on the network address…
  IP is about moving packets between networks
How can we actually get packets to/from hosts?

## Slide 4: Getting Packets Host-to-Host
Packet traverses source’s L2 network
If Hosts are on different networks, packet goes through one or more routers
  We just covered what happens here
Packet then traverses destination’s L2 network

## Slide 5: Basic Approach for Source
If destination host is on same L2 network
  Just send directly using L2 address
If destination host is on remote network
  Send to router on your L2 network
  It will then forward to destination’s network
How can you tell if destination host is remote?
  You know your IP address and mask
  You know destination’s IP address
  If they mask to the same network address, they are on same L2 network
Is this clear to everyone?

## Slide 6: Component Tasks
Assume we know IP address of destination (DNS)
Must know local information (DHCP)
  Own IP address and mask
  IP address of local router
  IP address of DNS server
  …
Must traverse L2 networks
  L2 network must work (spanning tree)
  Need to know which L2 addresses to use (ARP)

## Slide 7: This Lecture
Forwarding in L2
  Basic background on L2
  Spanning Trees
Discovery protocols
  ARP
  DHCP
Putting it all together in an example

## Slide 8: Background on Link-Layer

## Slide 9: Addressing at Link Layer
Link layer technologies use MAC addresses
There are very different from IP addresses…

## Slide 10: Medium Access Control Address
MAC address
  Numerical address associated with a network adapter
  Flat name space of 48 bits
    e.g., 00-15-C5-49-04-A9 in HEX
  Unique, hard-coded in the adapter when it is built
Hierarchical Allocation
  Blocks: assigned to vendors (e.g., Dell) by the IEEE
    First 24 bits (e.g., 00-15-C5-**-**-**)
  Adapter: assigned by the vendor from its block
    Last 24 bits

## Slide 11: MAC Address vs. IP Address
MAC addresses (used in link-layer)
  Hard-coded when adapter is built
  Flat name space of 48 bits (e.g., 00-0E-9B-6E-49-76)
    Like a social security number
  Portable, and can stay the same as the host moves
  Used to get packet between interfaces on same network
IP addresses
  Configured, or learned dynamically
  Hierarchical name space of 32 bits (e.g., 12.178.66.9)
    Like a postal mailing address
  Not portable, and depends on where the host is attached
  Used to get a packet to destination IP subnet

## Slide 12: Broadcast at Link-Level
Use broadcast address: ff:ff:ff:ff:ff:ff
Reaches everyone on L2 network

## Slide 13: Forwarding on Ethernet
As an example of L2

## Slide 14: Ethernet Uses Learning Switches
When a packet arrives at switch port X:
  Record X as the way to reach source of packet
  See if destination is in routing table
    If so, send out that port
    If not, flood out all other ports
Difference between flood and broadcast here
  Broadcast is an end: reach all hosts on network
  Flood is a means to reach a particular destination
    When you don’t know where that destination is, you flood all ports
    If next switch knows how to reach destination, it does not flood

## Slide 15: What does this require?
The flooding algorithm requires that the topology be a spanning tree:
  Spanning: must reach all nodes
  Tree: must not have loops
How do you turn an arbitrary topology into a spanning tree?
  You “turn off” certain links

## Slide 16: Consider graph

## Slide 17: A Spanning Tree

## Slide 18: Another Spanning Tree

## Slide 19: Yet Another Spanning Tree

## Slide 20: But how do you find such trees?

## Slide 21: A Chance for Redemption….
Do not look at sheet of paper until I say so
You will have five minutes to complete this task
Each sheet says:
You are node X You are connected to nodes Y,Z
Your job: Define spanning tree on this 40-node net
  You do so by crossing out some of your neighbors (and your neighbors must do the same to you)

## Slide 22: Ground Rules
You may not:
  Leave your seat (but you can stand)
  Pass your sheet of paper
  Let anyone copy your sheet of paper
You may:
  Ask nearby friends for advice
  Shout to other participants (anything you want)

## Slide 23: Go!

## Slide 24: Testing the Solution
Node X: stand up
  Who are you still connected to?
Those nodes, stand up: who are you still connected to (not counting X)?
Repeat….
Did anyone get called twice?
Did everyone get called?

## Slide 25: Doing it my way….
Pick an arbitrary root:
Construct shortest paths to root
Break ties by taking path with lowest ID next-hop
Here we go….

## Slide 26: Spanning Tree Protocol (Perlman‘85)
Protocol by which bridges construct a spanning tree
Nice properties
  Zero configuration (by operators or users)
  Self healing
Still used today

## Slide 27: Algorithm Has Two Aspects
Pick a root:
Destination to which shortest paths go
Pick the one with the smallest identifier (MAC addr.)
Compute shortest paths to the root:
No shortest path can have a cycle
Only keep the links on shortest-paths
  Break ties in some way if multiple shortest paths
Ethernet’s spanning tree construction does both with a single algorithm

## Slide 28: Breaking Ties
When there are multiple shortest paths to the root, choose the path that uses the neighbor switch with the lower ID.
One could use any tiebreaking system, but this is an easy one to remember and implement
  And please do remember it….

## Slide 29: Graph
1
2
3
4
5
6
7

## Slide 30: Links on spanning tree
3-1
5-1
6-1
2-3
4-2
7-2
1
2
3
4
5
6
7

## Slide 31: Node 1 Dies….
2
3
4
5
6
7

## Slide 32: Now what is the spanning tree?
2 is new root
3-2
6-2
4-2
7-2
5-6
2
3
4
5
6
7

## Slide 33: Constructing a Spanning Tree
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And advertising a distance d to Y
Switch selects node with smallest MAC as root
  Y in the messages (smallest switch has seen so far)
  Initially different nodes have different ideas about root
Switch discards links not on shortest path to root
  Based on d to Y in the messages

## Slide 34: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  I.e., switch X announces (X, 0, X) to its neighbors
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If Y’s id < current root: set root = Y
Switches compute their distance from the root
  Add 1 to the shortest distance received from a neighbor
If root or shortest distance to it changed, send neighbors updated message (Y, d+1, X)

## Slide 35: Example (root, dist, from)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(3,0,3)
(4,0,4)
(5,0,5)
(6,0,6)
(7,0,7)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,3)
(1,1,3)
(1,3,4)
(1,1,5)
(1,1,6)
(1,3,7)
✗
✗
✗

## Slide 36: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 37: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 38: Robustness of Algorithm
Algorithm must react to failures
  Failure of the root node
  Failure of other switches and links
Root switch sends periodic messages
  These declare itself as root
  Other switches forward messages in response
Detecting failures through timeout
  If no word from root, time out and claim to be the root!

## Slide 39: Example of Self-Stabilizing Algorithm
No matter how what the initial condition is
  State of links
  State in switches
If no additional failures/recoveries, then eventually the algorithm will converge to the right answer…
Requires:
  “Soft state”: state that times out if not refreshed
  “Always in recovery”: Constantly recomputing

## Slide 40: Questions?

## Slide 41: Where are we?
We now know a bit about L2:
  How to address
  How to forward in L2 and L3
  How to construct spanning trees
Now, how do we actually get a packet from one host to another host?
  Nodes need to know some basic information
  Rely on two discovery protocols
Later in course we will cover DNS
  How to get IP address of any host (by name)

## Slide 42: Two Discovery Protocols

## Slide 43: Discovery
A host is “born” knowing only its MAC address
Must discover lots of information before it can communicate with a remote host B
  what is my IP address?
  what is B’s IP address? (if B is remote)
  what is B’s MAC address? (if B is local)
  what is my first-hop router’s address? (if B is not local)
  …

## Slide 44: ARP and DHCP
Discovery protocols
  ARP  Address Resolution Protocol (at link layer)
  DHCP  Dynamic Host Configuration Protocol (app layer)
  Confined to a single local-area network (LAN)
  Rely on broadcast capability (as most discovery protocols)
Hosts
Router

## Slide 45: DHCP
“Dynamic Host Configuration Protocol”
  defined in RFC 2131
A host uses DHCP to discover
  its own IP address
  its netmask
  IP address(es) for its local DNS name server(s)
  IP address(es) for its first-hop “default” router(s)

## Slide 46: DHCP: operation
One or more local DHCP servers maintain required information
  IP address pool, netmask, DNS servers, etc.
  application that listens on UDP port 67

## Slide 47: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
  L2 broadcast, to MAC address FF:FF:FF:FF:FF:FF

## Slide 48: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message (broadcast)
  proposed IP address for client, lease time
  other parameters

## Slide 49: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message (broadcast)
Client broadcasts a DHCP request message
  specifies which offer it wants
  echoes accepted parameters
  other DHCP servers learn they were not chosen

## Slide 50: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message (broadcast)
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK

## Slide 51: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK
  (also broadcast)
(DHCP “relay agents” used when the DHCP server isn’t on the same broadcast domain -- see text)

## Slide 52: Sequence in more detail
Client: Server discovery message
Server: DHCP “offer” message
  Configuration parameters
    proposed IP address, mask, gateway router, DNS server, …
    Lease time (duration the information remains valid)
  Multiple servers may respond
    Multiple servers on the same broadcast network
Client: accepts one of the offers
  Client sends a DHCP “request” echoing the parameters
Server: “ACK” confirms request
  … and the other servers see they were not chosen
Why does a host need to know its mask?

## Slide 53: Dynamic Host Configuration Protocol
arriving client
DHCP server
203.1.2.5
DHCP discover
(broadcast)
DHCP offer
DHCP request
DHCP ACK
(broadcast)
Why all the broadcasts?
(there are exceptions)
(broadcast)
(broadcast)
How does DHCP send a broadcast?

## Slide 54: Sending Broadcasts
DHCP is at application layer
  Uses UDP transport protocol
IP does not support global broadcasts
  And DHCP only wants local broadcast
  Local broadcasts supported by layer 2 ff:ff:ff:ff:ff:ff
How to send local broadcast w/o violating layers?

## Slide 55: Local Broadcast at IP Level
Can't broadcast to all IP hosts
But application might want to “local” broadcast
Uses IP broadcast address 255.255.255.255
Link-layer then uses link-layer broadcast

## Slide 56: DHCP uses “soft state”
Soft state: if not refreshed, state is forgotten
  Hard state: state that is remembered until overwritten
Implementation:
  Address allocations are associated with a lease period
  Server: sets timer associated with record of allocation
  Client: must request refresh before lease period expires
  Server: resets timer when a refresh arrives; sends ACK
  Server: reclaims address when timer expires
Simple, yet robust under failure
  State always eventually fixes itself
  (harder to do with hard state)

## Slide 57: Soft state under failure
What happens when host XYZ fails?
  refreshes from XYZ stop
  server reclaims a.b.c.d after O(lease period)
Router
XYZ
DHCP Server
a.b.c.d is mine from (now, now+lease)
a.b.c.d is XYZ’s from (now, now+lease)

## Slide 58: Soft state under failure
What happens when server fails?
  ACKs from server stop
  XYZ releases address after lease, sends new request
  A new DHCP server can come up from a ‘cold start’
Router
XYZ
DHCP Server
a.b.c.d is mine from (now, now+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 59: Soft state under failure
What happens if the network fails?
  Refreshes and ACKs don’t get through
  XYZ release address; DHCP server reclaims it
Router
XYZ
DHCP Server
a.b.c.d is mine from (now, now+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 60: Hard State vs Soft State
It is essentially impossible to design simple hard-state protocols that can gracefully withstand:
  Network failures
  Server failures
  Host failures
When client or server crashes with state:
  Is that state valid when it comes back?
  How do others know whether they are coming back?

## Slide 61
Router
Host
Host
Host
Host
DHCP Server
Know enough for Host-to-Host?
DNS Server
What I learnt from DHCP
my IP: 1.2.3.48
netmask: 1.2.3.0/24 (255.255.255.0)
Local DNS: 1.2.3.156
router: 1.2.3.19

## Slide 62: Sending Packets Over Link-Layer
Link layer only understands MAC addresses
  Must translate destination IP address to MAC address
  Encapsulate IP packet in a link-level (Ethernet) frame
  But source only knows destinations IP address
Router
Host
Host
Host
Host
DNS
1.2.3.48
1.2.3.156
58-23-D7-FA-20-B0
90-E2-A1-09-66-1B
1.2.3.53
1.2.3.156
IP packet

## Slide 63: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consults the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate the (IP) packet with MAC header; transmit
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table

## Slide 64: ARP header
Bit offset
=1 for Ethernet
=0x0800 for IPv4
1=request; 2=reply
=6 for Ethernet
=4 for IPv4

## Slide 65: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does red host know about router’s adddress 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 66: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: Remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 67: Taking Stock: Naming
Layer | Examples | Structure | Configuration | Resolution Service
App. Layer | www.cs.berkeley.edu | organizational hierarchy | ~ manual | 
Network Layer | 123.45.6.78 | topological hierarchy | DHCP | 
Link layer | 45-CC-4E-12-F0-97 | vendor (flat) | hard-coded | 
DNS
ARP

## Slide 68: Example: A sending a packet to B
How does host A send an IP packet to host B?
A
R
B

## Slide 69: Example: A sending a packet to B
A
R
B
1. A sends packet to R. 2. R sends packet to B.

## Slide 70: A sends packet through router R
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP
A
R
B

## Slide 71: A sends packet through router R
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with E6-E9-00-17-BB-4B
Host A encapsulates the IP packet for B, and sends to R
A
R
B

## Slide 72: R Decides how to Forward Packet
Router R’s adapter receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adapter (port)
A
R
B
Two points:
  IP routing table points to this port
  Destination address is within mask of port’s address (i.e., local)

## Slide 73: R sends packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-56-2A
Router R encapsulates the packet and sends to B
A
R
B

## Slide 74: Next Week
Transport, NAT, DNS, etc…..