## Slide 1: CS 168 Congestion Control
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Congestion Control Overview
Everything in this lecture is oversimplified.
Lots of details omitted.
But the basic points remain valid….
Notes: Deceptively complicated….

## Slide 4: Flow Control vs Congestion Control
Flow control keeps one fast sender from overwhelming a slow receiver
Congestion control keeps a set of senders from overloading the network

## Slide 5: Congestion is Natural
Because Internet traffic is bursty!
  Stat mux cannot completely smooth out aggregate
If many packets arrive in a short period of time
  The node cannot keep up with the arriving traffic

## Slide 6: Congestion is Harmful
Average
Packet delay
Load
Typical queuing system with bursty arrivals
Must balance utilization versus delay and loss
Average
Packet loss
Load

## Slide 7: Huge Literature on Problem
In mid-80s Jacobson “saved” the Internet with CC
  His group and the DEC group came up with similar ideas
  His went right into BSD, and changed the world
Clean problem, infinite variations possible
Recent resurgence of interest after brief lag
  New methods (ML, performance-oriented)
  New context (datacenter networks)
  New pressure for high-performance
Notes: Congestion collapse

## Slide 8: Who Takes Care of Congestion?
Network?
End hosts?
Both?

## Slide 9: TCP’s Answer
End hosts adjust sending rate
Based on implicit feedback from network
Hosts probe network to test level of congestion
  Speed up when no congestion
  Slow down when congestion

## Slide 10: Drawbacks
Suboptimal (always above or below optimal point)
Relies on end system cooperation
Messy dynamics
  All end systems adjusting at the same time
  Large, complicated dynamical system
  Miraculous it works at all!
Ignores economics
  Who should get the bandwidth?

## Slide 11: Some History: TCP in the 1980s
Sending rate only limited by flow control
  Dropped packets  senders (repeatedly!) retransmit
Led to “congestion collapse” in Oct. 1986
  Throughput on the NSF network dropped from 32Kbits/s to 40bits/sec
“Fixed” by Van Jacobson’s development of TCP’s congestion control (CC) algorithms

## Slide 12: Van Jacobson
Leader of the networking research group at LBL
Many contributions to the early TCP/IP stack
  Most notably congestion control
Creator of many widely used network tools
  Traceroute, tcpdump, pathchar, Berkeley Packet Filter
Later Chief Scientist at Cisco, then Fellow at PARC
Now a member of the Borg (I mean Google)

## Slide 13: Jacobson’s Approach
Extend TCP’s existing window-based protocol but adapt the window size in response to congestion
A pragmatic and effective solution
  Required no upgrades to routers or applications!
  Patch of a few lines of code to TCP implementations
Extensively researched and improved upon
  Especially now with datacenters and cloud services

## Slide 14: All These Windows…
Congestion Window: CWND
  How many bytes can be sent without overflowing routers
  Computed by the sender using congestion control algorithm
Flow control window: AdvertisedWindow (RWND)
  How many bytes can be sent without overflowing receiver’s buffers
  Determined by the receiver and reported to the sender
Sender-side window = minimum{CWND, RWND}
  Assume for this lecture that RWND >> CWND

## Slide 15: Note
This lecture will talk about CWND in units of MSS
  (Recall MSS: Maximum Segment Size, the amount of payload data in a TCP packet)
  This is only for pedagogical purposes
Keep in mind that real implementations maintain CWND in bytes

## Slide 16: Basics of TCP Congestion Control
Congestion window (CWND)
  Maximum # of unacknowledged bytes to have in flight
Adapting the congestion window
  Increase upon lack of congestion: optimistic exploration
  Decrease upon detecting congestion
But how do you detect congestion?

## Slide 17: Detecting Congestion
Network could tell source (ICMP Source Quench)
  Risky, because during times of overload the signal itself could be dropped (and add to congestion)!
Packet delays go up (knee of load-delay curve)
  Tricky: noisy signal (delay often varies considerably)
Packet loss
  Fail-safe signal that TCP already has to detect
  Complication: non-congestive loss (checksum errors)

## Slide 18: Not All Losses the Same
Duplicate ACKs: isolated loss
  Still getting ACKs
Timeout: possible disaster
  Not enough dupacks
  Must have suffered several losses

## Slide 19: How to Adjust CWND?
Consequences of over-sized window much worse than having an under-sized window
  Over-sized window: packets dropped and retransmitted
  Under-sized window: somewhat lower throughput
Approach:
  Gentle increase when uncongested (exploration)
  Rapid decrease when congested

## Slide 20: AIMD
Additive increase
  On success of last window of data, increase by one MSS
Multiplicative decrease
  On loss of packet, divide congestion window in half

## Slide 21: Leads to the TCP “Sawtooth”
t
Window
halved
Loss
Notes: Picture not realistic!!

## Slide 22: This has been incredibly successful
Leads to the theoretical puzzle:
If TCP congestion control is the answer,
then what was the question?
The “question” has less to do with optimality than with:
  Asymmetric search
  Robustness over wide range of conditions

## Slide 23: Throughput Equation
In what follows refer to cwnd in units of MSS

## Slide 24: Calculation on Simple Model
Assume loss occurs whenever cwnd reaches W
  And detected by duplicate ACKs
Window: W/2, W/2+1, W/2+2, …W, W/2, …
  W/2 RTTs, then drop, then repeat
Average throughput: .75W(MSS/RTT)
  One packet dropped out of (W/2)*(3W/4)
  Packet drop rate p = (8/3) W-2
Throughput = (MSS/RTT) sqrt(3/2p)

## Slide 25: Some implications
Flows get throughput inversely proportional to RTT
  Fairness issue?
One can dispense with TCP and just match eqtn:
  Equation-based congestion control
  Measure drop percentage p, and set rate accordingly
  Useful for streaming applications

## Slide 26: How does this work at high speed?
Assume that RTT = 100ms, MSS=1500bytes
What value of p is required to go 100Gbps?
  Roughly 2 x 10-12
How long between drops?
  Roughly 16.6 hours
How much data has been sent in this time?
  Roughly 6 petabits
These are not practical numbers!

## Slide 27: Adapting TCP to High Speed
One approach: once speed is past some threshold, change equation to p-.8 rather than p-.5
We will return to this later in semester….

## Slide 28: Slow-Start
In what follows refer to cwnd in units of MSS

## Slide 29: AIMD Starts Too Slowly!
t
Window
It could take a long time to get started!
Need to start with a small CWND to avoid overloading the network.

## Slide 30: Bandwidth Discovery with Slow Start
Goal: estimate available bandwidth
  start slow (for safety)
  but ramp up quickly (for efficiency)
Consider
  RTT = 100ms, MSS=1000bytes
  Window size to fill 1Mbps of BW = 12.5 packets
  Window size to fill 1Gbps = 12,500 packets
  Either is possible!

## Slide 31: “Slow Start” Phase
Start with a small congestion window
  Initially, CWND is 1 MSS
  So, initial sending rate is MSS/RTT
That could be pretty wasteful
  Might be much less than the actual bandwidth
  Linear increase takes a long time to accelerate
Slow-start phase (actually “fast start”)
  Sender starts at a slow rate (hence the name)
  … but increases exponentially until first loss
Notes: MSS vs MTU??

## Slide 32: Slow Start in Action
Double CWND per round-trip time
Simple implementation:
on each ack, CWND += MSS
D
A
D
D
A
A
D
D
Src
Dest
D
D
1
2
4
3
A
A
A
A
8

## Slide 33: Slow Start and the TCP Sawtooth
Loss
Exponential “slow start”
t
Window
Why is it called slow-start? Because TCP originally had
no congestion control mechanism. The source would just start by sending a whole window’s worth of data.

## Slide 34: Slow-Start vs. AIMD
When does a sender stop Slow-Start and start Additive Increase?
Introduce a “slow start threshold” (ssthresh)
  Initialized to a large value
  On timeout, ssthresh = CWND/2
When CWND = ssthresh, sender switches from slow-start to AIMD-style increase

## Slide 35: Time Outs
In what follows refer to cwnd in units of MSS

## Slide 36: Loss Detected by Timeout
Sender starts a timer that runs for RTO seconds
Restart timer whenever ack for new data arrives
If timer expires:
  Set SSTHRESH  CWND / 2 (“Slow-Start Threshold”)
  Set CWND  1 (MSS)
  Retransmit first lost packet
  Execute Slow Start until CWND > SSTHRESH
  After which switch to Additive Increase

## Slide 37: Summary of Decrease
Cut CWND half on loss detected by dupacks
  “fast retransmit”
Cut CWND all the way to 1 (MSS) on timeout
  Set ssthresh to cwnd/2
Never drop CWND below 1 (MSS)

## Slide 38: Summary of Increase
“Slow-start”: increase cwnd by 1 (MSS) for each ack
Leave slow-start regime when either:
  cwnd > SSThresh
  Packet drop
Enter AIMD regime
  Increase by 1 (MSS) for each window’s worth of acked data

## Slide 39: Why AIMD?
In what follows refer to cwnd in units of MSS

## Slide 40: Three Congestion Control Challenges
Single flow adjusting to bottleneck bandwidth
  Without any a priori knowledge
  Could be a Gbps link; could be a modem
Single flow adjusting to variations in bandwidth
  When bandwidth decreases, must lower sending rate
  When bandwidth increases, must increase sending rate
Multiple flows sharing the bandwidth
  Must avoid overloading network
  And share bandwidth “fairly” among the flows

## Slide 41: Abstract View
Ignore internal structure of router and model it as a single queue for a particular input-output pair
Sending Host
Buffer in Router
Receiving Host
A
B

## Slide 42: 1. Discovering available bandwidth
Pick sending rate to match bottleneck bandwidth
  Without any a priori knowledge
  Could be gigabit link, could be a modem
A
B
100 Mbps

## Slide 43: 2. Adjusting to variations in bandwidth
Adjust rate to match instantaneous bandwidth
  Assuming you have rough idea of bandwidth
A
B
BW(t)

## Slide 44: 3. Multiple flows sharing bandwidth
Two Issues:
Adjust total sending rate to match bandwidth
Allocation of bandwidth between flows
A2
B2
BW(t)
A1
A3
B3
B1

## Slide 45: Reality
Congestion control is a resource allocation problem involving many flows, many links, and complicated global dynamics
1Gbps
600Mbps
1Gbps

## Slide 46: Problem #1: Single Flow, Fixed BW
Slow start is pretty good at this….
...no need to discuss further

## Slide 47: Problem #2: Single Flow, Varying BW
Want to track available bandwidth
Oscillate around its current value
If you never send more than your current rate, you won’t know if more bandwidth is available
Possible variations: (in terms of change per RTT)
Multiplicative increase or decrease:
  cwnd → cwnd * / a
Additive increase or decrease:
  cwnd → cwnd +- b

## Slide 48: Four alternatives
AIAD: gentle increase, gentle decrease
AIMD: gentle increase, drastic decrease
MIAD: drastic increase, gentle decrease
  too many losses: eliminate
MIMD: drastic increase and decrease
Notes: What do you think about these options?
Which one is obviously bad?
What do you think about the other ones?

## Slide 49: Problem #3: Multiple Flows
Want steady state to be “fair”
Many notions of fairness, but here just require two identical flows to end up with the same bandwidth
This eliminates MIMD and AIAD
  As we shall see…
AIMD is the only remaining solution!
  Not really, but close enough….

## Slide 50: Buffer and Window Dynamics
No congestion  x increases
Congestion  x decreases
A
B
C = 50 pkts/RTT
x

## Slide 51: Simple Model of Congestion Control
Two users
  rates x1 and x2
Congestion when x1+x2 > 1
Unused capacity when x1+x2 < 1
Fair when x1 =x2
User 1’s rate (x1)
User 2’s rate (x2)
Fairness line (x1 =x2)
Efficiency line (x1+x2 = 1)
1
1
congested 
 inefficient

## Slide 52: Example
User 1: x1
User 2: x2
fairness
line
efficiency
line
1
1
Inefficient: x1+x2=0.7
(0.2, 0.5)
Congested: x1+x2=1.2
(0.7, 0.5)
Efficient: x1+x2=1
Fair
(0.5, 0.5)
congested 
 inefficient
Efficient: x1+x2=1
Not fair
(0.7, 0.3)

## Slide 53: AIAD
Increase: x + aI
Decrease: x - aD
Does not converge to fairness
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(x1-aD,x2-aD)
(x1-aD+aI), x2-aD+aI))
congested 
 inefficient

## Slide 54: AIAD Sharing Dynamics
A
B
x1
D
E
x2

## Slide 55: MIMD
Increase: x*bI
Decrease: x*bD
Does not converge to fairness
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bdx1,bdx2)
(bIbDx1, bIbDx2)
congested 
 inefficient

## Slide 56: AIMD
(bDx1+aI, bDx2+aI)
Increase: x+aI
Decrease: x*bD
Converges to fairness
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
congested 
 inefficient

## Slide 57: AIMD Sharing Dynamics
A
50 pkts/sec
B
x1
D
E
Rates equalize  fair share
x2

## Slide 58: AIMD is only “fair” choice
But how fair is it?
Bandwidth depends on RTT
Hosts that send more flows get more bandwidth

## Slide 59: TCP Congestion Control Details

## Slide 60: Implementation
State at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  [Also dupACKcount and timer, as before]
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 61: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence after one RTT with no drops: CWND = 2xCWND

## Slide 62: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence after one RTT with no drops: CWND = CWND + 1
“Congestion Avoidance” phase (additive increase)

## Slide 63: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 64: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 65: Repeating Slow Start After Timeout
t
Window
Slow-start restart: Go back to CWND of 1 MSS, but take advantage of knowing the previous value of CWND.
Slow start in operation until it reaches half of previous CWND, I.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 66: One Final Phase: Fast Recovery
The problem: congestion avoidance too slow in recovering from an isolated loss

## Slide 67: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped
  What ACKs do they generate?
  And how does the sender respond?

## Slide 68: Timeline
ACK 101 (due to 102) cwnd=10 dupACK#1 (no xmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (no xmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (no xmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 + 1/5 (no xmit)
ACK 101 (due to 106) cwnd=5 + 2/5 (no xmit)
ACK 101 (due to 107) cwnd=5 + 3/5 (no xmit)
ACK 101 (due to 108) cwnd=5 + 4/5 (no xmit)
ACK 101 (due to 109) cwnd=5 + 5/5 (no xmit)
ACK 101 (due to 110) cwnd=6 + 1/5 (no xmit)
ACK 111 (due to 101)  only now can we transmit new packets
Plus no packets in flight so ACK “clocking” (to increase CWND) stalls for another RTT

## Slide 69: Solution: Fast Recovery
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount = 3
  ssthresh = cwnd/2
  cwnd = ssthresh + 3
While in fast recovery
  cwnd = cwnd + 1 for each additional duplicate ACK
Exit fast recovery after receiving new ACK
  set cwnd = ssthresh

## Slide 70: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK was for packet # 101
    i.e., receiver expecting next packet to have seq. no. 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 71: Timeline
ACK 101 (due to 102) cwnd=10 dup#1
ACK 101 (due to 103) cwnd=10 dup#2
ACK 101 (due to 104) cwnd=10 dup#3
REXMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd= 9 (no xmit)
ACK 101 (due to 106) cwnd=10 (no xmit)
ACK 101 (due to 107) cwnd=11 (xmit 111)
ACK 101 (due to 108) cwnd=12 (xmit 112)
ACK 101 (due to 109) cwnd=13 (xmit 113)
ACK 101 (due to 110) cwnd=14 (xmit 114)
ACK 111 (due to 101) cwnd = 5 (xmit 115)  exiting fast recovery
Packets 111-114 already in flight
ACK 112 (due to 111) cwnd = 5 + 1/5  back in congestion avoidance

## Slide 72: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 73: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 74: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 75: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 76: TCP Flavors
TCP-Tahoe
  CWND =1 on triple dupACK
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on triple dupack
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  incorporates selective acknowledgements
Our default assumption