## Slide 1: CS 168 Even More Congestion Control
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Announcements
Example with TCP without fast recovery is wrong
  Slide 40 is corrected and posted
Discussion of TCP-NewReno is right (our default)
Midterm regrades will be done over weekend
Today is about new CC designs
  I need the class to participate!

## Slide 4: A Critical Analysis of TCP

## Slide 5: The Many Failings of TCP CC
Cumulative ACKs are stupid
Fills up queues (large delays)
Depends on losses (noncongestive losses)
Does not scale to high-speed
Produces irregular saw-tooth behavior
Depends on RTT (unfair)
Takes a long time to reach steady state
Easy to cheat
Relies on homogeneity for performance/fairness

## Slide 6: (1) Cumulative ACK Stupidity
When we have cumulative ACKs, we must:
  Guess which data has arrived
  Play games with CWND to send additional packets
TCP SACK:
  Selective Acknowledgements
    Think: complete listing of all received packets
  Would remove need for “fast recovery”
Could design very simple CC algorithm
  Just slow-start, congestion avoidance, fast-retransmit
  Much more robust to drops (almost never time out)

## Slide 7: (2) TCP fills up queues
TCP only slows down when queues fill up
Means that delays are large for everyone
And many packets are dropped when buffer fills
  Not always, but it does tend to increase packet drops
Alternative: Random Early Drop (LBL)
  Drop packets on purpose before queue is full

## Slide 8: Random Early Drop (or Detection)
Measure avg queue size A with exp. weighting
  Allows short bursts of packets without over-reacting
Drop probability is a function of A
  No drops if A is very small
  Low drop rate for moderate A’s
  Drop everything if A is too big
Drop probability applied to incoming packets
Intuition: link is fully utilized well before buffer is full

## Slide 9: RED Dropping Probability

## Slide 10: Advantages of RED
Keeps queues smaller, while allowing bursts
  Just using small buffers in routers can’t do the latter
Reduces synchronization between flows
  Not all flows are dropping packets at once
  Increase/decrease are more gentle
Now being used to reduce buffer-bloat
  “buffer-bloat”: experiencing large delays
  Try uploading large file from home…
Notes: …

## Slide 11: Why Isn’t RED Fair?
RED gives all flows roughly the same drop rate
The TCP equation gives the following
Resulting throughputs depend on RTT…

## Slide 12: History of RED
RED proposed (Floyd and Jacobson)
  Huge support from research community
  Operators find it hard to configure, see few advantages
Adaptive RED (Floyd)
  Self-configuring version of RED. Largely ignored.
CoDel (Nichols and Jacobson)
  Cleaner self-configuring version of RED.
  Lots of press (bufferbloat)
Implementors adopt FQ-CoDel
  Karma’s a bitch!

## Slide 13: (3) Non-congestion-related Losses?
Can use Explicit Congestion Notification (ECN)
Bit in IP packet header (actually two)
  TCP receiver returns this bit in ACK
When RED router would drop, it sets bit instead
  Congestion semantics of bit exactly like that of drop
Advantages:
  Doesn’t confuse corruption with congestion
  Doesn’t confuse recovery with rate adjustment

## Slide 14: (4) Does AIMD work at high speed?
Throughput = (MSS/RTT) sqrt(3/2p)
  Assume that RTT = 100ms, MSS=1500bytes
What value of p is required to go 100Gbps?
  Roughly 2 x 10-12
How long between drops?
  Roughly 16.6 hours
How much data has been sent in this time?
  Roughly 6 petabits
These are not practical numbers!

## Slide 15: Adapting TCP to High Speed
One approach:
  Let AIMD “constants” depend on CWND
At very high speeds,
  Increase CWND by more than MSS in a RTT
  Decrease CWND by less than ½ after a loss
We will discuss other approaches later…

## Slide 16: High-Speed TCP Proposal (Floyd)
Bandwidth | AvgCwnd (pkts) | Increase a(w) | Decrease b(w)
1.5 Mbps | 12.5 | 1 | 0.50
10 Mbps | 83 | 1 | 0.50
100 Mbps | 833 | 6 | 0.35
1 Gbps | 8333 | 26 | 0.22
10 Gbps | 83333 | 70 | 0.10

## Slide 17: High-Speed TCP

## Slide 18: This changes the TCP Equation
Throughput ~ p-.8 (rather than p-.5)
  Packet drops every tens of seconds
To achieve high throughput:
  Don’t need such a tiny drop rate…
  Can ramp up more quickly
How can this coexist with normal TCP?
  Only invoke new parameters at large window sizes
  Competes fairly with normal TCP at normal speeds

## Slide 19: (5) Sawtooth Behavior Uneven
TCP throughput is “choppy”
  Repeated swings between W/2 to W
Some apps would prefer sending at a steady rate
  e.g., streaming apps
A solution: “Equation-Based Congestion Control”
  Ditch TCP’s increase/decrease rules and just follow the equation
  Measure drop percentage p, and set rate accordingly
Following the TCP equation ensures we’re “TCP friendly”
  i.e., use no more than TCP does in similar setting

## Slide 20: These Problems Are All Solved
With published and often standardized solutions
TCP-SACK
RED (and its many variants)
ECN
High-Speed TCP
Equation-based congestion control (EBCC)
Datagram congestion control protocol (DCCP)
Not widely used, as far as I know (but Apple just adopted ECN a few months ago!)

## Slide 21: Any Questions?

## Slide 22: (6) Bias Against Long RTTs
Flows get throughput inversely proportional to RTT
TCP unfair in the face of heterogeneous RTTs!
A1
A2
B2
B1
bottleneck
link
100ms
200ms

## Slide 23: Possible Solutions?
Make additive constant proportional to RTT
But people don’t really care about this….

## Slide 24: (7) How do short flows fare?
50% of flows have < 1500B to send; 80% < 100KB
Short flows are slowed down by slow-start
  It takes several round-trips to send 8 packets!
    Handshake, CWND=1, CWND=2, CWND=4, CWND=8
Too few packets to trigger dupACKs
  Isolated loss may lead to timeouts
At typical timeout values of ~500ms…
  ...might severely impact flow completion time

## Slide 25: Possible Solutions?
Larger initial window?
  Google proposed moving from ~4KB to ~15KB
  Covers ≈90% of HTTP Web
  Decreases delay by ~5%
Recursively cautious congestion control (RC3)
  Run normal TCP at normal priority
  Send aggressively at lower priorities
  With a limit on each priority level
  Ramps up to full speed immediately, no harm to others
  I failed at providing better QoS; this exploits worse QoS!

## Slide 26: (8) Cheating
TCP was designed assuming a cooperative world
No attempt was made to prevent cheating
Many ways to cheat, will present three

## Slide 27: Cheating #1: ACK-splitting (Rcvr)
Round-
Trip
Time
(RTT)
Sender
Receiver
ACK 486
Data 4381:5841
Data 1461:2921
Data 2921:4381
Data 5841:7301
ACK 973
ACK 1461
Data 1:1461
Rule: grow window by one
full-sized packet for each
valid ACK received
Send M (distinct) ACKs for one packet
Growth factor proportional
to M
What’s the fix?

## Slide 28: 10 line change to Linux TCP
(Courtesy of
Stefan Savage)

## Slide 29: Cheating #2: Increasing CWND Faster
Limit rates:
x = 2y
C
x
y
x increases by 2 per RTT
y increases by 1 per RTT

## Slide 30: Cheating #3: Open Many Connections
A
B
x
D
E
y
Assume
A starts 10 connections to B
D starts 1 connection to E
Each connection gets about the same throughput
Then A gets 10 times more throughput than D

## Slide 31: Cheating
Either sender or receiver can independently cheat!
Why hasn’t Internet suffered congestion collapse yet?
How can we prevent cheating?
  Verify TCP implementations?
  Controlling end points is hopeless!
So what should we do?

## Slide 32: (9) Converse of Cheating
To be fair, need to be TCP-friendly
Everyone uses “similar” CC algorithm
Slows down innovation!

## Slide 33: How do you solve these problems?
Bias against long RTTs
Slow to ramp up (for short flows)
Cheating
Need for uniformity

## Slide 34: Get the Network Involved!
Routers can help by:
  Providing guidance for speed to send at
  Providing isolation/fairness
Guidance for sending rate deals with
  Slow to ramp up
  Bias against long RTTs
Providing Isolation/Fairness deals with
  Cheating
  Need for uniformity

## Slide 35: Routers tell hosts how fast to send
Packets carry “rate field”
Routers insert “fair share” f in packet header
End-hosts set sending rate (or window size) to f
  Hopefully (still need some policing of endhosts!)
This is the basic idea behind the “Rate Control Protocol” (RCP) from Dukkipati et al. ’07

## Slide 36: A Few More Details
How does this work?
  Router estimates rate f that will use its capacity
  Adaptive process of guessing (why not exact?)
  This is what it tells hosts
Why does this work?
  Flows get immediately up to speed
  And no need to “probe” (gently or otherwise)
How do you evaluate the resulting performance?

## Slide 37: Flow Completion Time: TCP vs. RCP (Ignore XCP)
Flow Duration (secs) vs. Flow Size
RCP

## Slide 38: Why the improvement?

## Slide 39: Any Questions?

## Slide 40: How can routers ensure each flow gets its “fair share”?

## Slide 41: Isolation
Treat each “flow” separately
  For now, flows are packets between same Source/Dest.
Each flow has its own FIFO queue in router
Service flows in a round-robin fashion
  When line becomes free, take packet from next flow
Assuming all flows are sending MTU packets, all flows can get their fair share

## Slide 42: Benefits
Each flow can use their own adjustment algorithm
  Perhaps aided by the router telling them how fast to send
This solves the innovation problem!
  People can experiment with any CC algorithm
And the cheating problem!
  No matter what you do, you can’t get more than your share

## Slide 43: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 44: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 45: Fairness
When all flows want the same rate, fair is easy
  Fair share = C/N
  C = capacity of link
  N = number of flows
Notes:
  This is fair share per link. This is not a global fair share.
When not all flows have the same demand?
  Either flow isn’t high bandwidth
  Or limited by C/N on some other link

## Slide 46: Example 1
Requests: ri Allocations: ai
C=20
  Requests: r1=6, r2=5, r3=4
Solution: a1=6, a2=5, a3=4
When bandwidth is plentiful, everyone gets their request
This is the easy case

## Slide 47: Example 2
C=12
  Requests: r1=6, r2=5, r3=4
One solution: a1=4, a2=4, a3=4
  Everyone gets the same
Why not proportional to their demands?
  ai = (12/15)ri
Asking for more gets you more!
  Not incentive compatible (i.e., cheating works)

## Slide 48: Example 3
C=14; Requests: r1=6, r2=5, r3=4
a3=4 (can’t give more than a flow wants)
Remaining bandwidth is 10, with demands 6 and 5
  From previous example, if both want more than their share, they both get half
  a1=a2=5

## Slide 49: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
or set f to be infinite if no such value exists
This is what round-robin service gives
  if all packets are MTUs
Property:
  If you don’t get full demand, no one gets more than you
  Use it or lose it: you don’t get credit for not using link

## Slide 50: Example
Assume link speed C is 10mbps
Have three flows:
  Flow 1 is sending at a rate 8mbps
  Flow 2 is sending at a rate 6mbps
  Flow 3 is sending at a rate 2mbps
How much bandwidth should each get?
  According to max-min fairness?

## Slide 51: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 52: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 53: Dealing with different packet sizes
Mental model: Bit-by-bit round robin (“fluid flow”)
Can you do this in practice?
No, packets cannot be preempted
But we can approximate it
  This is what “fair queuing” routers do

## Slide 54: Fair Queuing (FQ)
For each packet, compute the time at which the last bit of a packet would have left the router if flows are served bit-by-bit
Then serve packets in the increasing order of their deadlines

## Slide 55: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Service
in fluid flow
system
FQ Packet
system
time
time
time
time

## Slide 56: Fair Queuing (FQ)
Implementation of round-robin generalized to case where not all packets are MTUs
Weighted fair queueing (WFQ) lets you assign different flows different shares
WFQ is implemented in almost all routers
  Not true in the 1980-90s, when CC was being developed
  Mostly used to isolate larger granularities (e.g., per-prefix)

## Slide 57: FQ vs. FIFO
FQ advantages:
  : cheating flows don’t benefit
  Bandwidth share does not depend on RTT
  Flows can pick any rate adjustment scheme they want
Disadvantages:
  More complex than FIFO: per flow queue/state, additional per-packet book-keeping

## Slide 58: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 59: Fairness Through Dropping
Traditional FQ uses scheduling to achieve fairness
But note that dropping is sufficient to give fairness
Assume a set of incoming rates ri
Dropping at rates pi = 1-f/ri yields fairness
ri(1-pi) = f

## Slide 60: Two Dropping Approaches
Estimate rate ri at edge, stick in packet header
  Then individual routers drop with probability 1=f/ri
  Where each router computes its on f
Estimate rate at every router using “shadow buffer”
  See how many packets of a flow are in shadow buffer
  Use this to estimate ri
  Why does this work?
  Implemented on significant fraction of Cisco product line

## Slide 61: Four Challenges
What is fair?
How to implement fairness in general
  Going beyond round-robin
Are there simpler ways to implement this?
And what’s wrong with this approach?

## Slide 62: Why is Scott a Moron?
Or why does Bob Briscoe think so?

## Slide 63: flow rate fairness dismantling a religion <draft-briscoe-tsvarea-fair-01.pdf>
Bob Briscoe
Chief Researcher, BT Group
IETF-68 tsvwg Mar 2007
status: individual draft
final intent: informational
intent next: tsvwg WG item after (or at) next draft

## Slide 64: Giving equal shares to “flows” is silly
What if you have 8 flows, and I have 4…
  Why should you get twice the bandwidth?
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why not penalize for using more scarce bandwidth?
And what is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 65: Charge people for congestion!
Use ECN as congestion markers
Whenever I get ECN bit set, I have to pay $$$
No debate over what a flow is, or what fair is…
Idea started by Frank Kelly, backed by much math
  Great idea: simple, elegant, effective
  Never going to happen…

## Slide 66: Summary of Router Assisted CC
Adjustment: helps get flows up to speed
  Huge improvement in FTC performance
Isolation: helps protect flows from cheaters
  Gives each flow fair share
  Allows innovation in CC algorithms

## Slide 67: Next Week
Interdomain routing (and multicast)