## Slide 1: CS 168 BGP and Advanced Routing
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Spring CS194
“Practical Networking” (168 is strict prereq.)
  Learn by building…..(only 20 students, take off WL)
  Builds on 168, does not repeat it
Taught by:
  Faculty: Sylvia Ratnasamy and Scott Shenker
  Researchers: Nick Weaver and Barath Raghavan
Content oriented around 3 or 4 projects
  Novel architectures
  Ad hoc wireless
  Packet processing (middleboxes)
  Monitoring (pretend to be NSA)
  …...

## Slide 4: Today’s Lecture
Problems in BGP (leftover from last lecture)
Multicast
Recent routing research
160 slides in total…..

## Slide 5: Border Gateway Protocol (BGP)
Issues with BGP

## Slide 6: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies
Relevance

## Slide 7: (1) Reachability
In normal routing, if graph is connected then reachability is assured
With policy routing, this does not always hold
AS 2
AS 3
AS 1
Provider
Provider
Customer

## Slide 8: Why Does the Internet Work?
Assumption 1: Policies obey Gao-Rexford
  Or at least are no more restrictive..
Assumption 2: Starting from any AS, and following the chain of providers, leads to a tier 1 ISP
  Tier 1: group of ISPs that all peer with each other
Under these assumptions, all ASes are connected
Proof?

## Slide 9: (2) Security
An AS can claim to serve a prefix that they actually don’t have a route to (blackholing traffic)
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
    How? What would you need?
Note: AS may forward packets along a route different from what is advertised
  Forcing the advertised paths to exist is doable
  Forcing an AS to use that path is much harder!
    Why?

## Slide 10: (3) Convergence
Result: If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge (safety)
For arbitrary policies, BGP may fail to converge!

## Slide 11: Example of Policy Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
“1” prefers “1 3 0”
over “1 0” to reach “0”

## Slide 12: Step-by-Step of Policy Oscillation
Initially: nodes 1, 2, 3 know only shortest path to 0
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0

## Slide 13
1 advertises its path 1 0 to 2
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 1 0
Step-by-Step of Policy Oscillation

## Slide 14
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 15
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 3 0
3 advertises its path 3 0 to 1
Step-by-Step of Policy Oscillation

## Slide 16
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 17
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 1 0
1 withdraws its path 1 0 from 2
Step-by-Step of Policy Oscillation

## Slide 18
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 19
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 2 0
2 advertises its path 2 0 to 3
Step-by-Step of Policy Oscillation

## Slide 20
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 21
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 3 0
3 withdraws its path 3 0 from 1
Step-by-Step of Policy Oscillation

## Slide 22
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 23
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
1 advertises its path 1 0 to 2
Step-by-Step of Policy Oscillation
advertise: 1 0

## Slide 24
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 25
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 2 0
2 withdraws its path 2 0 from 3
Step-by-Step of Policy Oscillation

## Slide 26
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
We are back to where we started!
And there is no stable state…..
Step-by-Step of Policy Oscillation

## Slide 27: How do these policies violate G-R?
Each prefers route through neighbor (over direct)
Thus, if 0 is a peer to all them, then
  1 must be 2’s customer (since 2 prefers 2-1-0 over 2-0)
  2 must be 3’s customer (since 3 prefers 3-2-0 over 3-0)
  3 must be 1’s customer (since 1 prefers 1-3-0 over 1-0)
Gao-Rexford requires that customer-provider graph is acyclic
  This example violate this!

## Slide 28: Policy Oscillations (cont’d)
Policy autonomy vs network stability
  Policy oscillations with even small degree of autonomy
  Focus of much recent research
Not an easy problem
  PSPACE-complete to decide whether given policies will eventually converge!
However, if policies follow normal business practices, stability is guaranteed
  “Gao-Rexford conditions”

## Slide 29: Theoretical Results (in more detail)
If preferences obey Gao-Rexford, BGP is safe
  Safe = guaranteed to converge
If there is no “dispute wheel”, BGP is safe
  But converse is not true
If there are two “stable states”, BGP is unsafe
  But converse is not true

## Slide 30: (4) Performance Nonissues
Internal routing (non)
  Domains typically use “hot potato” routing
  Not always optimal, but economically expedient
Policy not about performance (non)
  So policy-chosen paths aren’t shortest
AS path length can be misleading (non)
  20% of paths inflated by at least 5 router hops
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 31: Performance (example)
AS path length can be misleading
  An AS may have many router-level hops
AS 4
AS 3
AS 2
AS 1
BGP says that
path 4 1 is better
than path 3 2 1

## Slide 32: Real Performance Issue: Slow convergence
BGP outages are biggest source of Internet problems
Labovitz et al. SIGCOMM’97
    10% of routes available less than 95% of time
    Less than 35% of routes available 99.99% of the time
Labovitz et al. SIGCOMM 2000
    40% of path outages take 30+ minutes to repair
But most popular paths are very stable
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 33: BGP Route Recalculation
Many more paths need to be recomputed in BGP
  Compared to DV
Why?
This is part of BGP’s slowness to respond
  Large routing table updates
  Need to suppress rapid changes
  Path exploration (updates every time a new path is tested, not just when the distance changes)

## Slide 34: (5) BGP Misconfigurations
BGP protocol is both bloated and underspecified
  lots of attributes
  lots of leeway in how to set and interpret attributes
  necessary to allow autonomy, diverse policies
  but also gives operators plenty of rope
Much of this configuration is manual and ad hoc
And the core abstraction is fundamentally flawed
  disjoint per-router configuration to effect AS-wide policy
  now strong industry interest in changing this! [later: SDN]
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 35: (6) World of Policies Changing
ISPs are now “eyeball” and/or “content” ISPs
Less focus on “transit”, more on nature of customers
No systematic policy practices yet
  Details of peering arrangements are private
And interconnection points (IXPs) are replacing many pairwise peering arrangements

## Slide 36: BGP: How did we get here?
BGP was designed for a different time
  before commercial ISPs and their needs
  before address aggregation
  before multi-homing
We don’t get a second chance: `clean slate’ designs virtually impossible to deploy
Thought experiment: how would you design a policy-driven interdomain routing solution?
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 37: Multicast

## Slide 38: Motivating Example: Internet Radio
Internet concert
  More than 100,000 simultaneous online listeners
  Could we do this with parallel unicast streams?
Bandwidth usage
  If each stream was 1Mbps, concert requires > 100Gbps
Coordination
  Hard to keep track of each listener as they come and go
Multicast addresses both problems….

## Slide 39: Unicast approach does not scale…
Backbone
ISP
Broadcast
Center

## Slide 40: Instead build data replication trees
Backbone
ISP
Broadcast
Center
Copy data at routers
At most one copy of a data packet per link
LANs implement link layer multicast by broadcasting
Routers keep track of groups in real-time
Routers compute trees and forward packets along them

## Slide 41: Multicast Service Model
Receivers join multicast group with address G
Sender(s) send data to address G
Network routes data to each of the receivers
Multicast both delivery and rendezvous mechanism
  Senders don’t know list of receivers
  The latter is often more important than the former (why?)
R0 joins G
R1 joins G
Rn joins G
S
R0
R1
.
.
.
[G, data]
[G, data]
[G, data]
[G, data]
Rn
Net
Notes: Stay on this slide a bit…..

## Slide 42: Multicast and Layering
Multicast can be implemented at different layers
  Link layer
    e.g. Ethernet multicast
  Network layer
    e.g. IP multicast
  Application layer
    e.g. End system multicast
Each layer has advantages and disadvantages
  Link: easy to implement, limited scope
  IP: global scope, efficient, but hard to deploy
  Application: less efficient, easier to deploy [not covered]
Notes: Bandwidth plentiful in link; don’t worry about wasting

## Slide 43: Multicast Implementation Issues
How is join implemented?
How is send implemented?
How much state is kept and who keeps it?

## Slide 44: Link Layer Multicast
Join group at multicast address G
  NIC normally only listens for packets sent to unicast address A and broadcast address B
  After being instructed to join group G, NIC also listens for packets sent to multicast address G
Send to group G
  Packet is flooded on all LAN segments, like broadcast
Scalability:
  State: Only host NICs keep state about who has joined
  Bandwidth: Requires broadcast on all LAN segments
Limitation: just over single LAN

## Slide 45: Network Layer (IP) Multicast
Performs inter-network multicast routing
  Relies on link layer multicast for intra-network routing
Portion of IP address space reserved for multicast
  228 addresses for entire Internet
Open group membership
  Anyone can join (sends IGMP message)
    Internet Group Management Protocol
  Privacy preserved at application layer (encryption)
Anyone can send to group
  Even nonmembers

## Slide 46: How Would YOU Design this?
Take 5 minutes to design multicast
Requirements:
Receivers join group G
Senders send packet to destination G
Intradomain network routes packets to all receivers