## Slide 1: CS 168 Multicast and Routing Research
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Participation Count
203….which is less than half the class!
You have only yourself to blame....

## Slide 4: Multicast

## Slide 5: Multicast Implementation Issues
How is join implemented?
How is send implemented?
How much state is kept and who keeps it?

## Slide 6: Link Layer Multicast
Join group at multicast address G
  NIC = Network Interface Card
  NIC normally only listens for packets sent to unicast address A and broadcast address B
  After being instructed to join group G, NIC also listens for packets sent to multicast address G
Send to group G
  Packet is flooded on all LAN segments, like broadcast
Scalability:
  State: Only host NICs keep state about who has joined
  Bandwidth: Requires broadcast on all LAN segments
Limitation: just over single LAN

## Slide 7: Network Layer (IP) Multicast
Performs inter-network multicast routing
  Relies on link layer multicast for intra-network routing
Portion of IP address space reserved for multicast
  228 addresses for entire Internet
Open group membership
  Anyone can join (sends IGMP message)
    Internet Group Management Protocol
  Privacy preserved at application layer (encryption)
Anyone can send to group
  Even nonmembers

## Slide 8: How Would YOU Design this?
Requirements:
Receivers join group G (using IGMP message)
  Internet Group Management Protocol
Senders send packet to destination G
  With no knowledge of who the receivers are
Intradomain network routes packets to all receivers
  All the responsibility placed on the network

## Slide 9: IP Multicast Routing
Intra-domain (know the basics here)
  Source Specific Tree: Distance Vector Multicast Routing Protocol (DVRMP)
  Shared Tree: Core Based Tree (CBT)
  Single-Sender: SSM
Inter-domain [not covered]
  Very difficult…..

## Slide 10: Distance Vector Multicast Routing Protocol
Elegant extension to DV routing
Will cover two main steps in DVRMP
  Reverse Path Flooding
  Truncation (pruning)
Discussion is drastically oversimplified!

## Slide 11: General Strategy
Construct a tree from a source to all destinations
  This is done by using the reverse-paths from all destinations to the source
Packets sent along this tree
  Are copied when these tree splits
Why reverse paths?
  Forward paths from source to all destinations not guaranteed to be a tree
  Reverse paths are set of paths from all destinations to source, and this must be a tree (for dest-based routing)

## Slide 12: Reverse Path Flooding (RPF)
If incoming link is shortest path to source
Send on all links except incoming
Otherwise, drop
Issues:
Every link receives each multicast packet
Some links (LANs) may receive multiple copies
Can be avoided by knowing your parent in r-tree
s:2
s
s:1
s:3
s:2
s:3
r

## Slide 13: RPF is not enough!
This is a broadcast algorithm – the traffic goes everywhere
Need to “Prune” the tree when there are subtrees with no group members
Networks know they have members based on IGMP messages
Add the notion of “leaf” nodes in tree
  They start the pruning process

## Slide 14: Pruning Details
Prune (Source,Group) at leaf if no members
  Send Non-Membership Report (NMR) towards source
If all children of router R send NMR, prune (S,G)
  Propagate prune for (S,G) to parent of R
On timeout:
  Prune dropped
  Flow is reinstated
  Down stream routers re-prune
Note: a soft-state approach

## Slide 15: DVMRP Review
Packets are initially broadcast everywhere
  Using reverse paths to prevent loops
Leaf nodes send prunes if they have no members
  Prunes travel toward source (using forward path)
Result
  When all prunes have been sent (and none have timed out), then all packet from source S travel the subtree that connects S to all members of the group
    In the reverse direction!

## Slide 16: Distance Vector Multicast Scaling
State requirements:
  O(Sources  Groups) active state
How to get better scaling?
  Hierarchical Multicast
  Core-based Trees

## Slide 17: Core-Based Trees (CBT)
Pick “rendezvous point” for the group (called core)
Build tree from all members to that core
  (using forward-path unicast routing)
  Shared tree
More scalable:
  Reduces routing table state from O(S x G) to O(G)
  No initial flooding

## Slide 18: Establishing Shared Tree
Group members: M1, M2, M3
core
M1
M2
M3
control (join) messages

## Slide 19: Use Shared Tree for Delivery
Group members: M1, M2, M3
M1 sends data
core
M1
M2
M3
control (join) messages
data

## Slide 20: Core-Based Tree Approach
Build tree from all members to core or root
  Spanning tree of members
Packets are broadcast on tree
  We know how to broadcast on trees
Requires knowing core per group
  This is a problem in many settings
  Core must exist before members join
  But what if core is far from members?

## Slide 21: Special-Case: Single-Source Mcast
For each SSM group, only a single sender
  Which serves as the core (perfectly located!)
Well-suited to live event usage
  A natural single source
  Potential large audience for simultaneous reception

## Slide 22: Barriers to Multicast
Hard to change IP
  Multicast means changes to IP
    Unicast IP remains same, but IP now must include multicast
  Details of multicast were very hard to get right
    Years-long effort with many brilliant people
    Deering, Jacobson, Estrin, Handley, etc.
Not always consistent with ISP economic model
  Charging done at edge, but single packet from edge can explode into millions of packets within network

## Slide 23: Review of Multicast
DVMRP:
  Per-source trees (reverse path!)
  Flood then prune
  Issues: scalability (state) and flooding
CBT:
  Shared tree
  Built by receiver joins sent to core
  Any sender can reach tree by going to core

## Slide 24: Multicast vs Caching
If delivery need not be simultaneous, caching (as in CDNs) works well, and needs no change to IP
This is true for almost all online applications except:
  Gaming
  Videoconferences
  …..

## Slide 25: Recent Research in Routing

## Slide 26: Holy Trinity of Routing: LS, DV, PV
Normally presented as the complete story
But we know how to do much better
That is what we will talk about now…..
Notes: To complete analogy, Learning Switch is the Old Testament, before we saw the light….

## Slide 27: Major Routing Challenges:
Resilience (recovery without recomputation)
Traffic Engineering
Alternate approaches to BGP

## Slide 28: Routing Resilience

## Slide 29: Resilience
Basic routing algorithms rely on consistency or global convergence to ensure delivery
  LS: routers need to have same picture of network
  DV: if algorithm hasn’t converged, might loop
As nets grow, this gets harder and takes longer
  Need both consistency/convergence and timeliness!
Creates lag between failure detection and recovery
  Lag is biggest barrier to achieving 99.999% reliability

## Slide 30: Hacks Used Today
Preconfigured backup paths
  When link fails, router has a backup route to use
  Very helpful against single failures
  Only limited protection against multiple failures
  No systematic paradigm
ECMP: Equal-Cost Multipath
  Similar to backups, but narrower applicability
  Choose among several “shortest-paths”

## Slide 31: Solutions Presented Today
Failover routing
Multipath (one slide)
Failure-carrying packets
Routing-along-DAGs

## Slide 32: (1) Failover Routing
This is generalization of backup paths
  Routing based not just on destination, but on incoming port
Simple form: routing table for packet coming in a particular port for dest D lists several outgoing ports
  Port X, Port Y, Port Z, ….
Semantics: for a packet coming in port A, for dest D
  If port X is up, use it
  If port X is down, use port Y
  If port X and port Y are down, use port Z
  ....

## Slide 33: Amazing Fact
No one had studied the power of this approach
  Some work looking at partial methods….
Current conjecture: if graph G is k-connected, then one can find a set of failover routing tables such that G can withstand any k-1 link failures.
Status of conjecture (for more general form)
  We have proven this for k=1, 2, 3, 4, 5
  We have no idea how to make progress for k > 5
  If someone in this class proves the conjecture for general k, you can have my house.

## Slide 34: (2) Multipath Routing
Multipath:
  Providing more than one path for each S-D pair
  Allow endpoints to choose among them
    This can be implemented by having a “path” field in packet
Good: if one path goes down, can use another
Bad: Delay while endpoints detect failure (RTT)
Absolutely necessary because of E2E arguments
  But still has RTT’s worth of delay before recovery…
Part of solution, but still need more reliable routing

## Slide 35: Fundamental Question
Can we completely eliminate the need to “reconverge” after link failures?
i.e., can we tolerate failures without losses, as long as network remains connected?

## Slide 36: Failure-Carrying Packets (FCP)

## Slide 37: FCP Approach: Step 1
Ensure all routers have consistent view of network
  But this view can be out-of-date
  Consistency is easy if timeliness not required
Use reliable flooding so all events reach all nodes
  Nodes can construct series of network maps
  Each map has sequence number (don’t ask how…)
Routers write this number in packet headers, so packets are routed according to the same “map”

## Slide 38: Forwarding and Map Numbers
Each node has sequence of maps 1, 2,…
  But may not have the most recent
When packet arrives, it carries a map #
  If node has this map, it forwards packet using this map
  If node does not have this map, it forwards using its most recent map, and writes (lower) map # in packet
Eventually all routers use same map to route packet
This achieves consistency, but not timeliness….
  Because old maps may not have recent failures….

## Slide 39: FCP Approach: Step 2
Carry failure information in the packets!
  Use this information to “fix” the old maps
When a packet arrives and the next-hop link for the path computed with the consistent state is down, insert failure information into packet header
  Then compute new paths assuming that link is down
If failure persists, it will be included in next consistent picture of network
  Then not needed in packet header

## Slide 40: Example: FCP routing
B
D
C
E
A
F
IP packet
source
destination

## Slide 41: Example: FCP routing
F
B
D
C
E
A
source
destination
IP packet
(C,E)
IP packet
(D,F)
(C,E)
IP packet

## Slide 42: Class Exercise: Prove This Works
Develop line of argument about why this guarantees connectivity
Under what circumstances does guarantee hold?

## Slide 43: Keys to Proof
Deadend: as long as map plus failures has connectivity, no dead ends
Loops: Assume loop. The nodes on the loop all share the same “consistent” map plus a set of failures in the packet header. Therefore, they compute the same path. Contradiction.

## Slide 44: Condition for Correctness
Consider a set of changes to network from the last consistent map before packet is sent until TTL of packet would expire.
If intersection of all network states during change process is connected, then FCP will deliver packet

## Slide 45: Properties of FCP
Guarantees packet delivery
  As long as a path exists during failure process
Major conceptual change
  Don’t rely solely on protocols to keep state consistent
  Information carried in packets ensures eventual consistency of route computation
  Ion’s Stoica’s thesis!

## Slide 46: Results: OSPF vs. FCP
Unlike FCP, OSPF cannot simultaneously provide low churn and high availability
Overhead [msgs/sec per link]
OSPF-overhead
FCP-lossrate
OSPF-lossrate

## Slide 47: Results: Backup-paths vs. FCP
Unlike FCP, Backup-paths cannot simultaneously provide low state and loss rate
Bkup-state
FCP-state
FCP-loss rate
Bkup-lossrate

## Slide 48: Problems with FCP
Requires changes to packet header
  And packet headers could get long
Requires fast recomputation of routes
  Can precompute common cases, but worst case is bad
Does not address traffic engineering
  What is that?

## Slide 49: Traffic Engineering (TE)
Connectivity is necessary but not sufficient
Need to also provide decent service
Requires that links on the path not be overloaded
  Congestion control lowers drop rate, but need to provide reasonable bandwidth to connections by spreading load
TE is a way of distributing load on the network
  i.e., not all packets travel the “shortest path”
Currently done by spreading load over MPLS paths

## Slide 50: Multiprotocol Label Switching (MPLS)
Operators wanted more flexibility in routing traffic
  Normal routing just used destination address…
Wanted ability to route on larger aggregates
  First decide if flow belongs to aggregate, then route agg.
  Example: all traffic from LA to NY follow same path
Wanted ability to route at finer granularity
  Not all packets with same destination take same path
Solution: insert a “label” before IP header
  Route based on that label

## Slide 51: MPLS Header

## Slide 52: Using MPLS
Make a distinction between edge and core routers
Edge routers inspect IP header, insert MPLS label
Core routers route based on MPLS label
Must set up forwarding state for MPLS labels
  Done in a variety of ways, for a variety of goals
  Supporting failover paths, TE,…

## Slide 53: MPLS is widely used
Sometimes used for traffic engineering
But mostly used for VPNs
  Where all a customer’s traffic is given a single label
Extremely important practically, not intellectually
  Because it is not tightly tied to a single purpose
  Each use is ad hoc, rather than an overall paradigm
    Sort of like the IPv6 flow ID: all mechanism, no policy

## Slide 54: MPLS and TE
MPLS:
  Enables operators to nail up paths between two points
  Think of an MPLS tunnel as a virtual link (layer 2.5)
Most modern backbones are built out of MPLS
  With backup paths to deal with failure
Load is spread by having multiple MPLS paths between any two points, and then adjusting how load is split between them….
OK for backbone, but not generally (TE or failure)

## Slide 55: Routing Along DAGs (RAD)

## Slide 56: Avoiding Recomputation: Take II
Recover from failures without global recomputation
Support locally adaptive traffic engineering
Without any change in packet headers, etc.
Or requiring major on-the-fly route recomputation

## Slide 57: Background
Focus only on routing table for single destination
  Could be a prefix, or a single address
  Routing to each destination is independent, so this is fine
Today we compute paths to particular destination
  From each source to this destination there is a path
When path breaks, need to recompute path
  The source of all our troubles!

## Slide 58: Our Approach: Shift the Paradigm
Move from path to DAG (Directed Acyclic Graph)
Routing compute paths from source to destination
If a link fails, all affected paths must be recomputed
Path
DAG
X
X
  Packets can be sent on any of the DAG’s outgoing links
  No need for global recomputation after each failure

## Slide 59: DAG Properties
Guaranteed loop-free
Local decision for failure recovery
Adaptive load balancing
X
X
0.7
0.3

## Slide 60: Load Balancing
Use local decisions:
  Choose which outgoing links to use
  Decide how to spread the load across these links
  Push back when all outgoing links are congested
    Send congestion signal on incoming links to upstream nodes
Theorem:
  When all traffic goes to a single destination, local load balancing leads to optimal throughput
Simulations:
  In general settings, local load balancing close to optimal

## Slide 61: DAG-based Routing
Essentially a principled paradigm for backup paths
  Can tolerate many failures
  Scalable
  Easy to understand and manage
Notes: MPLS: 100,000s of labels….

## Slide 62: Computing DAG
Use each link in a single direction
DAG iff link directions follow global order
Computing a DAG for destination v is simple:
  Essentially a shortest-path computation
  With consistent method of breaking ties

## Slide 63: What about Connectivity?
Multiple outgoing links improve connectivity
  But can RAD give “perfect” connectivity?
If all outbound links fail that node is disconnected
  Even if underlying graph is still connected
How can we fix this?

## Slide 64: Link Reversal
If all outgoing links fail, reverse incoming links to outgoing
X
X
X
X
Notes: pre compute paths doesn’t have guarantee
but link reversal can

## Slide 65: RAD Algorithm
When packet arrives, send out any outgoing link
When an outgoing link fails (or is reversed)
  If other outgoing links exist, do nothing
  If no other outgoing links exist, reverse all incoming links
    i.e., change them to outgoing

## Slide 66: Link Reversal Properties
Connectivity guaranteed!
  If graph is connected, link reversal process will restore connectivity in DAG
  Without ever creating any loops!
This has been known in wireless literature
  Now being applied to wired networks
If you don’t think this is neat, then you are asleep.
  Local rule to produce ideal connectivity!

## Slide 67: Class Exercise: Prove This Works
Develop line of argument about why this guarantees connectivity

## Slide 68: Keys to Proof
Deadend: algorithm never results in dead-ends
  At least one link will be outbound, if you have a link
Loops:
  Assume network does not have loop at beginning
    (i.e., we have a DAG)
  Link reversal cannot create a loop
    Because reversed node cannot be part of a loop
  Therefore, topology never in a state where a loop exists
Are we done with proof?

## Slide 69: No, link reversals might not terminate
Must prove topology reaches fixed point
  If underlying graph is connected
Not reaching a fixed point means process of node reversals continues forever
Since network is of finite size, this process must repeat in a cycle of node reversals
How can we prove this is impossible?

## Slide 70: Fact #1
If a node has a path to the destination, then it will never reverse itself.
Conclusion: the set of nodes with a path to the destination is nondecreasing

## Slide 71: Fact #2
For a node to do a second link reversal, all of its neighbors must have also reversed its links.
Therefore, the set of nodes doing a link reversal is an expanding set
Can only re-reverse all reversing nodes if the process reaches the “edge” of network
But once this process touches a node which is connected to the source, it stops. QED.

## Slide 72: Summary of RAD
Local responses lead to:
  Guaranteed connectivity
  Close-to-optimal load balancing
Can be used for L2 and/or L3
  No change in packet headers

## Slide 73: Why Isn’t RAD Enough?
The link reversals are on the “control plane”
They take time to take effect
  Going to the CPU on the router ~10msec
Packets can be lost in the meantime…
Exactly the problem with FCP route recomputation
  Works on control-plane speeds, not data speeds

## Slide 74: Data-Driven Connectivity (DDC)
Define link reversal properties in terms of actions that can occur at data speeds
Events: packet arriving in “reverse” direction
Action: remove that link from outgoing set
Goal: define simple algorithms that can be supported in HW
  We think we have such a design….

## Slide 75: A Completely Different Approach to BGP

## Slide 76: BGP Was a Misbegotten Child
ASes (domains) not part of original architecture
  IP was intended to connect relatively large “networks”
  But as subnets became much smaller units…
  …ASes became this larger granularity of interconnection
ASes had novel requirements:
  Autonomy: ability to set own routing policy (flexibly)
  Privacy: need not announce the policy to others
BGP invented in ‘89 to meet these requirements
  BGP’s distributed execution model provides both

## Slide 77: Problems with This Approach
Execution model embeds particular policy model
  Would be hard to implement other policy models
Convergence problems
  These are typically addressed locally
    MRAI timers, flapping thresholds, etc.
Can’t evaluate impact of potential changes
  Vulnerabilities
  Planned outages
Notes: So we were thinking about alternatives to BGP, and we hit on the following crazy idea…

## Slide 78: A “Crazy” Idea
Decouple policy model from execution model
Achieve autonomy and privacy through cryptography
  Secure Multi-Party Computation (SMPC)

## Slide 79: Essence of SMPC (Outsourcing Model)
Group of people have personal secrets Si and want to compute some F(S) without giving secrets away
  Use k “secure servers” (a,b,c,…) to do computation
Everyone breaks secret into k “shares” Sia, Sib, Sic…
  And send them to the appropriate server
Servers execute a distributed computation on shares
  Local computation on {Sa}, distributed with other servers
Then hand back results Ria to each person
  {Ri} enough to compute personal result Fi(S)

## Slide 80: In the End….
Everyone knows personal result Fi(S), nothing else
The servers know nothing
Approach provides both autonomy and privacy
  Independent of the function F

## Slide 81: Simple Example
Five PIs want to compute their total salary (for grant)
  But don’t want to give away their individual salaries
Have three “secure servers” at their disposal

## Slide 82: Breaking Up Secrets into “Shares”
PI1 $107 = 25 + 92 – 10
PI2 $105 = -445 + 93 + 457
PI3 $98 = 4 + 99 – 5
PI4 $100 = 25 + 30 + 45
PI5 $90 = 32 + 29 + 29

## Slide 83: Sending Shares to Servers
PI1 $107 = _ _ _ _ _ _
PI2 $105
PI3 $98
PI4 $100
PI5 $90
25
92
-10
+
Notes: Add slide where the three servers add their results, then send the results back to each server.

## Slide 84: When All Nodes Do This
Each server a has share Sia from each node
Servers add their shares: Ta = S1a + S2a + S3a….
Send results Ta back to nodes:
Each node can calculate total!
  T = Ta + Tb + Tc
Each node knows total, but not individual salaries.
Servers know nothing

## Slide 85: SMPC Is Far More General
SMPC can compute any function of inputs Si
But general computation is quite complicated

## Slide 86: Application to BGP
AS i’s secret consists of: (per destination)
  Import: Preference ranking over all of i’s possible routes
  Export: Routes AS is willing to make available to peer j
AS i’s personal result: (per destination)
  Next-hop on path

## Slide 87: Practical Issues
Computational servers:
  Large commercial clusters (Amazon, MSoft, Google,…)
  Have multiple sets of clusters for redundancy
Bootstrap:
  Use normal BGP to construct routes to/from servers
  Or global anycast is domains are willing to forgo policies

## Slide 88: Resulting Design
Domains have complete autonomy, privacy
  Have more privacy than today
Simple convergence behavior
  Send updates to clusters, get back new paths
Policy model not tied to computational model
  Can be fully general (theoretically)

## Slide 89: Key Question: Is this computationally feasible?
Answer: not quite, but we are getting close…..

## Slide 90: Next Lecture
Multiple Access
Network Security