## Slide 1: CS 168 Multiple Access and Security
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Some History
Ethernet was invented as a broadcast technology
  Each packet received by all attached hosts
Easy to set up, cheap to build
  But hosts had to share channel (multiple access)
Current Ethernets are “switched”
  No sharing
But sharing a channel is conceptually important
  Multiple access is also used in wireless

## Slide 4: Multiple Access Control (MAC)
Single shared broadcast channel
  Must avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
  Need distributed algorithm for sharing the channel
  Algorithm determines which node can transmit
Classes of techniques
  Channel partitioning: divide channel into pieces
  Taking turns: scheme for trading off who gets to transmit
  Random access: allow collisions, and then recover
We focus on this last approach (most Internet-like!)

## Slide 5: Random Access MAC Protocols
When node has packet to send
  Transmit at full channel data rate
  No a priori coordination among nodes
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies:
  How to detect collisions
  How to recover from collisions
Examples
  ALOHA and Slotted ALOHA (background)
  CSMA, CSMA/CD, CSMA/CA (used in practice)

## Slide 6: Key Ideas of Random Access
Carrier sense
  Listen before speaking, and don’t interrupt
  Checking if someone else is already sending data
  … and waiting till the other node is done
Collision detection
  If someone else starts talking at the same time, stop
    But make sure everyone knows there was a collision!
  Realizing when two nodes are transmitting at once
  …by detecting that the data transmission is garbled
Randomness
  Don’t start talking again right away
  Waiting for a random time before trying again

## Slide 7: Where it all Started: AlohaNet
Norm Abramson left Stanford in 1970
  So he could surf!
Set up first data communication system for Hawaiian islands
  Hub at U. Hawaii, Oahu
Had two radio channels:
  Random access:
    Sites sending data
  Broadcast:
    Hub rebroadcasting data
Notes: Who is he, and why is he my hero?

## Slide 8: Aloha Signaling
Two channels: random access, broadcast
Sites send packets to hub (random)
  If received, hub sends ACK (random)
  If not received (due to collision), site resends
Hub sends packets to all sites (broadcast)
  Sites can receive even if they are also sending
Questions:
  When do you resend? Resend with probability p
  How does this perform? Need a clean model….

## Slide 9: Slotted ALOHA
Assumptions
All frames same size
Time divided into equal slots (time to transmit a frame)
Nodes are synchronized
Nodes begin to transmit frames only at start of slots
If multiple nodes transmit, nodes detect collision
Operation
When node gets fresh data, transmits in next slot
No collision: success!
Collision: node retransmits on each slot with probability p until success

## Slide 10: Slot-by-Slot Example

## Slide 11: Efficiency of Slotted Aloha
Suppose N stations have packets to send
  Each transmits in slot with probability p
Probability of successful transmission: by a particular node i: Si = p (1-p)(N-1) by any of N nodes: S= N p (1-p)(N-1)
What value of p maximizes prob. of success:
  For fixed p, S  0 as N increases
  But if p = 1/N, then S  1/e = 0.37 as N increases
Max efficiency is only slightly greater than 1/3!

## Slide 12: Pros and Cons of Slotted Aloha
Pros
Single active node can continuously transmit at full rate of channel
Highly decentralized: only need slot synchronization
Simple
Cons
Wasted slots:
  Idle
  Collisions
Collisions consume entire slot
Clock synchronization
Pros
Single active node can continuously transmit at full rate of channel
Highly decentralized: only need slot synchronization
Simple
Notes: Why is clock synchonization necessary?
It isn’t, but if we get rid of it, efficiency goes down…

## Slide 13: Improving on Slotted Aloha for Enet
Fewer wasted slots
  Need to decrease collisions and empty slots
Don’t waste full slots on collisions
  Need to decrease time to detect collisions
Avoid need for synchronization
  Synchronization is hard to achieve
  And Aloha performance drops if you don’t have slots
Notes: Which of these are the most important!

## Slide 14: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does this eliminate all collisions?
  No, because of nonzero propagation delay

## Slide 15: CSMA Collisions
Propagation delay: two nodes may not hear each other’s before sending.
Would slots hurt or help?
CSMA reduces but does not eliminate collisions
Biggest remaining problem?
Collisions still take full slot!
How do you fix that?
Notes: Ask: who knows? (from knowing ethernet)?
Someone who doesn’t, how to do this?
Listen before sending to detect possible collision
Why not listen to detect current collision!

## Slide 16: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired LANs:
  Compare transmitted, received signals
Collision detection difficult in wireless LANs:
  Reception shut off while transmitting (well, perhaps not)
  Not perfect broadcast (limited range) so collisions local
  Leads to use of collision avoidance instead
    Will discuss in later in lecture

## Slide 17: CSMA/CD Collision Detection
B and D can tell that collision occurred.
Note: for this to work, need restrictions on minimum frame size and maximum distance.
Why?
Notes: Draw failed collision detection….

## Slide 18: Limits on CSMA/CD Network Length
Latency depends on physical length of link
  Time to propagate a packet from one end to the other
Suppose A sends a packet at time t
  And B sees an idle line at a time just before t+d
  … so B happily starts transmitting a packet
B detects a collision, and sends jamming signal
  But A can’t see collision until t+2d
latency d
A
B

## Slide 19: Limits on CSMA/CD Network Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions. E.g., for 10 Mbps Ethernet:
  Maximum length of the wire: 2,500 meters
  Minimum length of a frame: 512 bits (64 bytes)
    512 bits = 51.2 sec (at 10 Mbit/sec)
    For light in vacuum, 51.2 sec ≈ 15,000 meters vs. 5,000 meters “round trip” to wait for collision
  What about 10Gbps Ethernet?
latency d
A
B
Notes: 10Gbps is switched, doesn’t have this problem!!!

## Slide 20: Performance of CSMA/CD
Time wasted in collisions
  Proportional to distance d
Time spend transmitting a packet
  Packet length p divided by bandwidth b
Rough estimate for efficiency (K some constant)
Note:
  For large packets, small distances, E ~ 1
  As bandwidth increases, E decreases
  That is why high-speed LANs are all switched
Notes: K represents number of collisions per transmission….

## Slide 21: Ethernet Multiple Access
First widely deployed multiple access

## Slide 22: Benefits of Ethernet
Easy to administer and maintain
Inexpensive
Increasingly higher speed
Evolvable!

## Slide 23: Evolution of Ethernet
Changed everything except the frame format
  From single coaxial cable to hub-based star
  From shared media to switches
  From electrical signaling to optical
Lesson #1
  The right interface can accommodate many changes
  Implementation is hidden behind interface
Lesson #2
  Really hard to displace the dominant technology
  Slight performance improvements are not enough

## Slide 24: Ethernet: CSMA/CD Protocol
Carrier sense: wait for link to be idle
Collision detection: listen while transmitting
  No collision: transmission successful
  Collision: abort transmission & send jam signal
Random access: binary exponential back-off
  After collision, wait a random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again
    Using min packet size as “slot”
  If transmission occurring when ready to send, wait until end of transmission (CSMA)

## Slide 25: Binary Exponential Backoff (BEB)
Think of time as divided in slots
After each collision, pick a slot randomly within next 2m slots
  Where m is the number of collisions since last successful transmission
Questions:
  Why backoff?
  Why random?
  Why 2m?
Notes: How would listening help?

## Slide 26: Behavior of BEB Under Light Load
Look at collisions between two nodes
First collision: pick one of the next two slots
  Chance of success after first collision: 50%
Second collision: pick one of the next four slots
  Chance of success after second collision: 75%
In general: after mth collision
  Chance of success: 1-2-m
  But the delay also increases with m….

## Slide 27: BEB: Theory vs Reality
In theory, there is no difference between theory and practice. But, in practice, there is.

## Slide 28: BEB Reality
Performs well (far from optimal, but no one cares)
  Large packets are ~23 times as large as minimal slot
Is mostly irrelevant
  Almost all current ethernets are switched

## Slide 29: BEB Theory
A very interesting algorithm
Stability for finite N only proved in 1985
  Ethernet can handle nonzero traffic load without collapse
    Greenberg et al. (AT&T)
All backoff algorithms unstable for infinite N (1985)
  Poisson model: infinite user pool, total demand is finite
    David Aldous (UCB Statistics)
Not of practical interest, but gives important insight
  Multiple access should be in your “bag of tricks”
Notes: e.g., know most important way to spread a rumor…

## Slide 30: Question
Two hosts, each with infinite packets to send
What happens under BEB?
Throughput high or low?
Bandwidth shared equally or not?

## Slide 31: MAC “Channel Capture” in BEB
Finite chance that first one to have a successful transmission will never relinquish the channel
  The other host will never send a packet
Therefore, asymptotically channel is fully utilized and completely allocated to one host

## Slide 32: Example
Two hosts, each with infinite packets to send
  Slot 1: collision
  Slot 2: each resends with prob ½
    Assume host A sends, host B does not
  Slot 3: A and B both send (collision)
  Slot 4: A sends with probability ½, B with prob. ¼
    Assume A sends, B does not
  Slot 5: A definitely sends, B sends with prob. ¼
    Assume collision
  Slot 6: A sends with probability ½, B with prob. 1/8
Conclusion: if A gets through first, the prob. of B sending successfully halves with each collision

## Slide 33: Another Question
Hosts now have large but finite # packets to send
What happens under BEB?
Throughput high or low?

## Slide 34: Answer
Efficiency less than one, no matter how many packets
Time you wait for loser to start is proportional to time winner was sending….

## Slide 35: Different Backoff Functions
Exponential: backoff ~ ai
  Channel capture?
  Efficiency?
Superlinear polynomial: backoff ~ ip p>1
  Channel capture?
  Efficiency?
Sublinear polynomial: backoff ~ ip p≤1
  Channel capture?
  Efficiency?

## Slide 36: Different Backoff Functions
Exponential: backoff ~ ai
  Channel capture (loser might not send until winner idle)
  Efficiency less than 1 (time wasted waiting for loser to start)
Superlinear polynomial: backoff ~ ip p>1
  Channel capture
  Efficiency is 1 (for any finite # of hosts N)
Sublinear polynomial: backoff ~ ip p≤1
  No channel capture (loser not shut out)
  Efficiency is less than 1 (and goes to zero for large N)
    Time wasted resolving collisions

## Slide 37: Why Do I Care?
Why do you like music?
It makes me happy….
But also, until this work was done, no one knew about capture, or what properties of the backoff enabled it.
You don’t understand something until you’ve played with it. Just getting it to work isn’t enough.
Notes: E.g., knowing how to spread rumor

## Slide 38: Network Security
narrowly defined….

## Slide 39: My definition of “network security”
“network security” ≠ “security in a connected world”
  For the latter, take CS 161 (spectacular course!)
If network magically transfers data between known parties, there is no “network security” problem
There are many other security problems
  Distributed system (if A lies to B, does system crash?)
  Operating system (Can A’s system be compromised?)
  …
But these may not require network solutions

## Slide 40: A few non-network security issues
Browser “drive-by” exploits
Server vulnerabilities
Spam
Phishing
Account theft
….

## Slide 41: Two Kinds of Network Security Goals
Core concern: accomplishing communication
  Getting the data from A to B intact
  Knowing it was from intended party, to intended party
Also: Keeping bystanders as ignorant as possible
  Making sure C, D, etc. don’t know what A and B did

## Slide 42: Core Security Requirements
Availability: Will the network deliver data?
Authentication: Who is sending me data?
Integrity: Do messages arrive in original form?
Provenance: Who is responsible for this data?
  Not who sent the data, but who created it
  Important because communication may not be directly between actors, but through intermediaries

## Slide 43: Keeping Bystanders Ignorant
Privacy: can others read data I send?
Anonymity: can I avoid revealing my identity?
Freedom from traffic analysis: can someone tell when I am sending and to whom?
Today, will ignore latter two and focus on privacy

## Slide 44: Back to other goals
Availability
Authentication
Integrity
Provenance
Privacy

## Slide 45: Public Key Crypto Provides
Way to authenticate yourself: signature
Way to ensure privacy: encryption
  with rcvr’s public key
Way to verify integrity: hash function (or MAC)
Way to verify provenance: signature
In short, crypto provides all but availability!
  Will return to availability later, focus on crypto for now

## Slide 46: On Cryptography and Identities

## Slide 47: Crypto is about algorithms…..
…algorithms that enable or prevent certain actions
  Enable authentication and provenance
  Prevent eavesdropping and undetectable tampering
But security also requires tying actions to identities
  Who is contacting me?
And identities are not purely algorithmic

## Slide 48: Three Aspects of Identities
Real-world identities (RWI)
  This is who you are in the real world
  RWI established by social interactions
    Direct experience
    Referrals from friends
    ….
Names
  Used in network protocols (e.g., DNS, URLs)
Keys
  Used by crypto

## Slide 49: Security requires binding all three…
Protocols: to ensure that they are interacting with appropriate entity, name must be bound to key
  When accessing CNN.com, I need to know CNN’s key in order to make sure that I’m not being spoofed
Humans: to ensure that they are interacting with appropriate entity, name must be bound to RWI
  I need to know that CNN.com is the news organization based in Atlanta, not the Canadian Numismatic Network
Once names are bound to both keys and RWI
  Then keys and RWI are indirectly bound together

## Slide 50: Current Approach
Google, human interactions: bind RWI to names
  Works pretty well when you start with RWI and find name
  Works less well when presented with name…
    …and you are left to guess the RWI (phishing!)
Certificate authorities bind names to keys
  Binding is done via digital certificates
  This does not work well…

## Slide 51: The evolution of a cynic….
“Commercial certificate authorities protect you from anyone from whom they are unwilling to take money.”
  Matt Blaze 2001
“A decade ago, I observed that commercial certificate authorities protect you from whom they are unwilling to take money. That turns out to be wrong; they don’t even do that much.”
  Matt Blaze 2010

## Slide 52: Deeper problem with this approach
Network: needs binding between names and key
  Fetches data based on name
  Authenticates based on keys
Human: needs binding between RWI and name
  Human makes decisions based on RWI
  Humans must be involved in anything concerning RWI
Current approach requires external authority to make the binding the network needs
  Ties network infrastructure to external authorities

## Slide 53: An Alternative Approach
Use self-certifying names
  Make your name the hash of your public key
  Then the binding between names and keys is inherent
  The network need not turn to external authorities
Binding between RWI and names is flexible
  Requires human-level interactions and judgements
    How do I decide a name represents my brother?
    Does same mechanism give name representing Barack Obama?
  Already done reasonably well by Google, etc.
  But is independent of low-level network mechanisms
    So it can evolve!
    Different people can use different mechanisms

## Slide 54: Trust vs Identity
Knowing who you are dealing with is different than trusting them
Trust is a completely different concept, that should lie outside the architecture
We often refer to mechanisms that bind names to keys or RWIs as “trust” mechanisms
  Terrible terminology

## Slide 55: Back to other goals
Availability
Authentication
Integrity
Provenance
Privacy

## Slide 56: Only One Crypto Can’t Handle….
Availability
Authentication
Integrity
Provenance
Privacy

## Slide 57: Protecting Availability

## Slide 58: How can availability be harmed?
Problems in basic protocols
  Persistent outages due to natural events
External vulnerabilities in basic protocols
  Attackers can prevent protocols from functioning
Internal vulnerabilities in basic protocols
  If attackers compromise routers, can prevent network from functioning
Denial-of-service attacks
  Overwhelming the data plane with traffic

## Slide 59: How Can We Avoid These?
Problems in basic protocols
  Good design and careful operation
External vulnerabilities in basic protocols
  Good design and careful operation
Internal vulnerabilities in basic protocols
  Good design and careful operation
Denial-of-service attacks
  Requires new thinking….

## Slide 60: Denial of Service (DoS)
Attacker prevents legitimate users from using something (network, server)
Motives?
  Retaliation
  Extortion (e.g., betting sites just before big matches)
  Commercial advantage (disable your competitor)
  Cripple defenses (e.g., firewall) to enable broader attack
Often done via some form of flooding
Can be done at different semantic levels
  Network: clog a link or router with a huge rate of packets
  Transport: overwhelm victim’s ability to handle connections
  Application: overwhelm victim’s ability to handle requests

## Slide 61: DoS: Network Flooding
Goal is to clog network link(s) leading to victim
  Either fill the link, or overwhelm their routers
  Users can’t access victim server due to congestion
Attacker sends traffic to victim as fast as possible
  It will often use (many) spoofed source addresses …
Using multiple hosts (slaves, or zombies) yields a Distributed Denial-of-Service attack, aka DDoS
Traffic is varied (sources, destinations, ports, length) so no simple filter matches it
If attacker has enough slaves, often doesn’t need to spoof - victim can’t shut them down anyway! :-(

## Slide 62: Distributed Denial-of-Service (DDoS)
Master
Slave 1
Slave 3
Slave 4
Slave 2
Victim
Control traffic directs slaves at victim
src = random dst = victim
Slaves send streams of traffic (perhaps spoofed) to victim

## Slide 63: Very Nasty DoS Attack: Reflectors
Reflection
  Cause one non-compromised host to help flood another
  E.g., host A sends DNS request or TCP SYN with source V to server R.
Reflector (R)
Internet
Attacker (A)
R
V
Victim (V)

## Slide 64: Very Nasty DoS Attack: Reflectors
Reflection
  Cause one non-compromised host to attack another
  E.g., host A sends DNS request or TCP SYN with source V to server R.
  R sends reply to V
Reflector (R)
Internet
Attacker (A)
V
R
Victim (V)

## Slide 65: Diffuse DDoS: Reflector Attack
Master
Slave 1
Slave 3
Slave 4
Slave 2
Victim
Control traffic directs slaves at victim & reflectors
Request: src = victim dst = reflector
Reflectors send streams of non-spoofed but unsolicited traffic to victim
Reflector 1
Reflector 9
Reflector 4
Reflector 2
Reflector 3
Reflector 5
Reflector 6
Reflector 7
Reflector 11
Reflector 8
Reflector 10
Reply: src = reflector dst = victim

## Slide 66: Defending Against Network Flooding
How do we defend against such floods?
Answer: basically, we don’t! Big problem today!
Techniques exist to trace spoofed traffic back to origins, but this isn’t useful in face of a large attack
Techniques exist to filter traffic, but a well-designed flooding stream defies stateless filtering
Best solutions to date:
  Overprovision - have enough raw capacity that it’s hard to flood your links
    Largest confirmed botnet to date: 1.5 million hosts (old!)
    Floods seen to date: 40+ Gbps (old!)
  Distribute your services - force attacker to flood many points
    E.g., the root name servers

## Slide 67: Architectural Approaches to DDoS?
Later in semester….