## Slide 1: CS 168 Rethinking the Internet Architecture
Fall 2015
Scott Shenker
http://inst.eecs.berkeley.edu/~cs168/fa15/

## Slide 2
Ssssshhhhhhhhhhhhhhh

## Slide 3: Office Hours
Today: after class (in Soda 415, not classroom)
Thursday: after class (in Soda 415)
Reading week: review sessions T/Th in this classroom
  No prepared slides
  Submit questions by email beforehand

## Slide 4: Today’s Agenda
If you could redesign the Internet architecture from scratch, what would you change?
Consider this question in two steps:
What are the biggest problems you see?
How would you address these problems?
What follows is my personal take on these issues

## Slide 5: Warning
This material goes beyond anything in book
And it might be hard to follow at times
But:
  You’ve seen parts of this before
  And please ask if you don’t understand
And:
  If you follow this lecture, you will know more about Internet architecture than 99% of networking researchers!

## Slide 6: Problems with Today’s Architecture
“Accidents”
  Aspects widely used before seriously designed
  Or had to be redesigned under severe constraints
Oversights
  Issues that were never seriously considered
Open questions
  Issues that remain unanswered today….

## Slide 7: “Accidental” Aspects of Architecture
Addressing, multihoming, and aggregation
  Scaling relies on aligning allocation and topology
  No one would pretend CIDR is a fundamental design
    LPM is not just an optimization, but needed for correctness!
Naming
  Designed for scaling and autonomy, not authentication
Crucial aspects largely ignored by architecture
  Domains
  Middleboxes

## Slide 8: Implications of Middleboxes/Domains
Domains:
  Original network architecture: hosts/networks
  New network reality: hosts/networks/domains
  While addresses are broken into host/network components, there is no “domain” component”
Middleboxes:
  People think that mboxes violate E2E principle
  But mboxes are right, and the E2E principle is wrong
  Wrong for functionality that is not host-oriented

## Slide 9: Oversights
Evolution: how do you change the architecture
  The version number in IP doesn’t address all the issues
DDoS: preventing denial-of-service attacks
  Nothing in today’s architecture helps with this

## Slide 10: A Big Open Question
Is packet delivery right interface for the Internet?
Some believe put-get is a better interface:
  Put: publish content, so others can retrieve
  Get: retrieve specified content (from nearest location)
  Information-centric networking (ICN)
    Interface is host-content, not host-host
Others advocate delay-tolerant networking (DTN)
  Make no assumption about ends both being up
  Put-get makes delay-tolerant networking easier
    Since there is no host-to-host interface

## Slide 11: How I would address these problems
Step#1: Change naming
  Provide basis for authentication without certificates
Step#2: Change basic addressing
  Integrate domains into architecture
Step #3: Change how we build networks
  Making middleboxes part of the architecture
  Enable domains to support new protocols
Step #4: Solve the evolution problem
  Identify and avoid the barriers to evolution
  And let history decide what’s the right interface….

## Slide 12: Internet Naming: Take 2
Repeats past material….

## Slide 13: Three Aspects of Identities
Real-world identities (RWI)
  This is who you are in the real world
  RWI established by social interactions
    Direct experience
    Referrals from friends
    ….
Names
  Used in network protocols (e.g., DNS, URLs)
Keys
  Used by crypto

## Slide 14: Security requires binding all three…
Protocols: to ensure that they are interacting with appropriate entity, name must be bound to key
  When accessing CNN.com, I need to know CNN’s key in order to make sure that I’m not being spoofed
Humans: to ensure that they are interacting with appropriate entity, name must be bound to RWI
  I need to know that CNN.com is the news organization based in Atlanta, not the Canadian Numismatic Network
Once names are bound to both keys and RWI
  Then keys and RWI are indirectly bound together

## Slide 15: Current Approach
Google, human interactions: bind RWI to names
  Works pretty well when you start with RWI and find name
  Works less well when presented with name…
    …and you are left to guess the RWI (phishing!)
Certificate authorities bind names to keys
  Binding is done via digital certificates
  This does not work well…

## Slide 16: Deeper problem with this approach
Network: needs binding between names and key
  Fetches data based on name
  Authenticates based on keys
Human: needs binding between RWI and name
  Human makes decisions based on RWI
  Humans must be involved in anything concerning RWI
Current approach requires external authority to make the binding the network needs
  Ties network infrastructure to external authorities

## Slide 17: An Alternative Naming Approach
Use self-certifying names
  Make your name the hash of your public key
  Then the binding between names and keys is inherent
  The network need not turn to external authorities
Binding between RWI and names is flexible
  Requires human-level interactions and judgments
    How do I decide a name represents my brother?
    Does same mechanism give name representing Barack Obama?
  Already done reasonably well by Google, etc.
  But is independent of low-level network mechanisms
    So it can evolve!
    Different people can use different mechanisms

## Slide 18: Problems with this approach?
Scaling: names are “flat”
  But Google can resolve flat names at scale
Recall: how can I remember a 256-bit name?
  Names used by network not those exposed to humans
  People have private set of human-readable names
  Private HRN to RWI mappings
Key compromise: (or lack of uniqueness)
  Must register key (in Google-like database)
  When used for access, etc., usage is stored there
  Can negate a key if detect problem (cannot be undone)

## Slide 19: Paradigm Change
Can always check whether entity belongs to the name they claim to belong to
  By forcing them to sign with key bound to name
  This helps in the design of secure protocol
All other aspects of naming are outside the architecture (and need not be standardized)
  Search engines, name registries, etc.

## Slide 20: Internet Addressing: Take 2
Repeats past material…

## Slide 21: New Addressing Architecture
Addresses are of the form: A:B:C:H
H is the name of the end host (or interface)
A, B, C, etc are routable “regions”
  Outermost address must be globally routable (domain)
  B must be routable within A
  C must be routable within B
All addresses are hashes of associated public key

## Slide 22: Forwarding
Basic correctness: A:B:C:H
  Route towards A
  Once inside A, route towards B
  …
Optimization:
  Can always look ahead to “deeper” match
  Still looking for exact matches, so easier than LPM
Note: LPM is harder and needed for correctness
  Deepest match is easier, and an optimization

## Slide 23: Scaling
Multihoming is natural:
  DNS (or its replacement) can offer multiple addresses
  E.g., A:H and B:H get you to the same host
Aggregation is flexible:
  Can insert aggregation levels: change A:H to A:B:H
  Aggregation independent of topology and allocation

## Slide 24: Interdomain Routing
Routes computed in terms of domains A
  Can then easily build BGP security into protocol
    Sign route advertisements
Host can belong to multiple domains
  A:H, B:H
  Interdomain routing need not worry about multihoming
  It just carries packets to specified domain
Doesn’t solve all conceptual problems with interdomain routing, but does clean it up…

## Slide 25: DDoS Prevention
DDoS attacks leverage compromised hosts
  Owners are benign, but host is compromised
Have NICs support “shut-off” packets (SOP)
  H1 can tell H2 to not send it any more packets
  Request is processed by the NIC
  Compromised OS can’t prevent enforcement
SOPs can be verified
  H1 can prove it sent the packet
  And can prove it has a packet from H2

## Slide 26: How SOPs Work
First-hop routers verify host addresses
  No spoofing possible
When host receives unwanted packet, it sends SOP
  Includes portion of unwanted packet
  Signs payload
Receiving NIC can verify:
  That it sent an unwanted packet
  That the SOP is from the recipient

## Slide 27: Obvious Problem?
Can I fool a victim into sending me a packet, and then send an SOP to the victim?
  This would prevent the victim from shutting off attackers
Even if H1 is banned from sending packets to H2, it is allowed to send SOPs to H2
  At a slow rate, so it does not constitute an attack

## Slide 28: Paradigm Change
Internet service model is not just:
  Anyone can send a packet to anyone
It is now:
  Anyone can send a packet to anyone, unless the recipient expressly asks to not receive packets from sender

## Slide 29: Network Infrastructure: Take 2

## Slide 30: Current Network (Domain) Design
Two main ingredients:
  HW switches/routers
  HW middleboxes
Only supports protocols designed into boxes
To deploy new middleboxes, must insert new HW
  CAPEX
  OPEX
Inflexible in both placement and protocols!

## Slide 31: New Approach: HW Core, SW Edge
Build domain core with traditional HW
  Handles forwarding (unicast, anycast, multicast) and TE
Build domain edge with SW (x86), handling all else:
  Isolation, access control, virtualization, …
  Middleboxes
Domain has edge clusters and switched core:
  Clusters at edge run middleboxes in VMs (or equivalent)
  Core is based on HW switches/routers

## Slide 32: Flexibility
Middleboxes: just spin up a VM
Protocols:
  Support all internetwork (L3) protocols at edge
  Use an L2 protocol for all internal forwarding
Supporting new L3 protocols via edge SW
  No internal changes needed!
  But do need changes to hosts (later in lecture)

## Slide 33: Paradigm Change
Build domains the way we build networks:
  External protocol is internetwork protocol
  Internal protocol is “private” protocol
    Could be IP, or IPv6, or whatever
No exposed internal addresses besides hosts H
  Host addresses H are location-independent
Domains have great:
  Flexibility: can implement new protocols/mboxes in SW
  Autonomy: can implement whatever they want internally

## Slide 34: Software vs Hardware
We are not claiming that software forwarding is as fast or cost effective as hardware forwarding
  2 orders of magnitude difference, perhaps growing?
We only claim that edge forwarding requirements can be met with software
  Estimates: large ISPs have ~10Tbps of edge bandwidth
  This entails $150,000 of infrastructure (for min-sized pkts)
  This barely pays for a single mid-range router
The HW vs SW debate isn’t over which is faster
  It is over whether HW is necessary at the edge
  And whether complex functionality is necessary in core

## Slide 35: Implications
Note that most network functionality driven by SW
SW comes in several kinds:
  Mbox code (at edge)
  SDN controller code (managing domain)
  Other packet processing at edge (new protocols)
None of it is tied to particular boxes
Network functionality will move at the speed of SW!
  Biggest change in networking since the Internet!

## Slide 36: Evolution: Take 1

## Slide 37: Evolution: Changing the Architecture
Changing the architecture without “flag day” requires coexistence of architectures
Coexistence of new architectures is necessary and sufficient for evolution, so we focus on this
But supporting a new architectures requires changing many components….

## Slide 38: Supporting New Architecture Requires Changing Many Components
Some are relatively easy:
  Host OS, router software support, new applications
Some are moderately hard, but doable
  Router hardware support, domain deployment
  But much easier with new domain design….
Others are extremely hard: (architectural “anchors”)
  “Legacy” applications
  Universal agreement (e.g., interdomain routing/addressing)
Notes: Change requiring first two: feasible
Requiring last: infeasible.

## Slide 39: How Do These Impede Innovation?
Internet architecture typically described in layers
But that picture ignores the “structure” of the Internet
Can look at the Internet a different way…

## Slide 40: A New Way of Looking at Architecture
Domain
Application
Network Stack
Rest of Internet (via BGP)
IP

## Slide 41: Rigidity of Current Architecture
Domain
Application
Network Stack
Rest of Internet (via BGP)
IP

## Slide 42: The Design Question
Can we evolve without changing the “anchors”?
This is key distinction between feasible and infeasible
  If have to change anchors, there is little hope for evolution

## Slide 43: The Answer
Yes, just ensure design is modular and extensible
Extensibility: functionality w/ backwards compatibility
  Deploy functionality in parallel, let apps/stacks choose
Modularity: no implementation details in interfaces
  Only expose necessary semantics
Entire design: apply principles to two anchor interfaces
  Network API (netAPI) and Interdomain services

## Slide 44: Design of Network API
Modular: keep networking details out of interface
  Let stack resolve names, understand network details, etc.
Extensible: put “schema” identifier in netAPI
  Schemas represent different API styles
  Updated applications can invoke new functionality

## Slide 45: Example Schemas
Schema ID | Primitives | Data Structure
Sockets | open, connect, accept, read, write, close | Bytes
Publish/Subscribe | publish, subscribe | Publications
RPC | send_request receive_request | Function call and response
Multimedia | play | Audio/video frames
… | … | …
Only standardizing Schema ID
the way applications specify their choice of schema
(a trivial level of indirection)

## Slide 46: How Are These Schemas Supported?
Some can be supported by end host
  RPC-like schema merely moves functionality into stack
But others “require” network support
  E.g., Information-centric network (ICN) designs “require” network to support put/get interface
New Interdomain service models (ISMs)
  Agreement between some domains on new network functionality

## Slide 47: Interdomain Service Models (ISMs)
Methods of communicating across domains
  Ucast/mcast/acast packet delivery
  Delay-tolerant networks
  ICN (e.g., DONA, NDN, etc.)
ISMs handle all interdomain issues
  Domain addressing, routing (if applicable)
  DoS, congestion control, etc.
ISMs do not dictate intradomain design
  The implementation of an ISM might affect domain design
  But definition of an ISM does not dictate domain design

## Slide 48: Design Principles
Extensible:
  “Packets” carry ISM identifier telling domain how to handle
  Thus, can have many ISMs running in parallel
Modular:
  Host only aware of syntax and semantics of ISM “header”
  Does not need to be aware of ISM implementation

## Slide 49: Partial Deployment and Compatibility
If an entity’s domain hasn’t implemented ISM then:
  Sender gets “unreachable” message, tries another ISM
  Or host can “join” ISM by tunneling through to ISM node
For two hosts to communicate, they:
  Must use compatible host-level protocols (transport, etc.)
  Must be connected by at least one ISM path
    ISM reachability may be visible (depends on ISM)
Notes: Applies to content-oriented ISMs as well (in terms of unreachable)

## Slide 50: Provides Framework For Evolution
Only standardize syntax for specifying ISM, Schema
  No need for global agreement on anything more
Clean separation btwn domain internals and ISMs
  Domains can use any internal technology to support ISMs
  Can choose what ISMs to support
Clean separation btwn applications and network
  Network can evolve without application’s knowledge
Claim: this is enough to make innovation feasible

## Slide 51: The New Internet
Domain
Application
Network Stack
Rest of Internet
ISMs
netAPI
Network stack and domain have complete freedom to innovate
Notes: Mention IPv6 as in network stack/domain: seamless….

## Slide 52: Huh?
Can think of this as making everything within a domain an L2 protocol
  No need for agreement on L2 technologies
ISMs can be deployed in parallel
  Need basic connectivity ISM (e.g., IP) for tunneling
  Then can have subsets of domains supporting an ISM
  Global agreement not necessary
ISMs handle interdomain addressing
  Domains can adopt their own intradomain addressing
  This is where IP failed!

## Slide 53: Don’t We Need a Narrow Waist?
Each ISM needs a narrow waist
  The waist is what all participating domains agree on
But there can be more than one such waist
The fact that we thought we needed only one waist is because we use IP for both interdomain and intradomain communication
  Cerf/Kahn got this right (when domains were networks)
  We messed this up when domains and networks diverged

## Slide 54: Why Is This So Simple?
Internet is built around great abstractions
Evolution was impeded by unfortunate interfaces
  Neither modular nor extensible
  Can be fixed with a small amount of engineering…
Evolution isn’t mysterious, if you get out of the way!
  Can freely change intradomain architectures
  Can incrementally add new Interdomain service models
  Many ISMs can coexist!

## Slide 55: Incentives for Innovation
This design enables:
  Hosts to choose which of several ISMs to use
  Domains to adopt ISMs without global agreement
Allows domains to compete on “features”
  Domains not supporting an ISM may give worse service
  If ISM doesn’t give better service, not worth deploying

## Slide 56: Summary
What was once seen as a tautological impossibility
  Architecture is what we all agree on
  How can we possibly change it without a flag day
Can be seen as almost inevitable consequence of good design practice

## Slide 57: Scorecard of Problems
Aggregation/Multihoming/Domains: solved
DDoS: solved
Middleboxes: solved
Evolution: solved
In fact, multiple architectures can coexist!

## Slide 58: Vision of Future
Network designs will be:
  Modular
  Extensible
Networks will be built out of:
  Commodity HW
  Third-party SW
Network functionality will be deployed in SW
And networks will finally be like other systems